## Slide 1: Korea-4GSR Project Overview and Current Progress in LLRF Development
Chong Shik Park, Ph.D
Korea University, Sejong
Department of Accelerator Science and Accelerator Research Center
On behalf of Korea-4GSR Group
Korea-France Collaboration Meeting on a LLRF Noise Reduction
Jan. 29, 2026

## Slide 2: Overview of the Korea-4GSR Project
Beam Energy | 4 GeV
Beam Emittance | less than 100 pm·rad (Design: 62 pm·rad)
Circumference | 800 m
Beamlines | 10 in the first phase (more than 40 in final phase)
Accelerator | Gun, Injector LINAC, 4 GeV Booster and Storage Ring
Lattice | Hybrid 7 Bend Achromat (H7BA)
- | Normal conducting RF cavity and 500 MHz
Land & Building
Location
Period & Budget
Period | 2021~2029
Budget | 1.1643 Trillion KRW = USD 834 M
Land | 540,000 m2
Building | 69,959 m2
Location | Ochang, Cheongju-si, Chungcheongbuk-do
Characteristics
Location of Ochang
Seoul
Daejeon
Pohang
Ochang

## Slide 3: Korea-4GSR Project Timeline
2021 | 2022 | 2023 | 2024 | 2025 | 2026 | 2027 | 2028 | 2029 | 2030
Design Review
Korea-4GSR(Multipurpose Synchrotron Radiation Construction) Project
Accelerator & Beamlines
Site Construction
Building Design
Building & Facility Construction
CDR
TDR
Installation
Commissioning
Operation
1st
3rd
2nd

## Slide 4: Machine Parameters
 | SR Ring Parameter | Vaule
 | Energy [GeV] | 4.0
 | Beam current [mA] | 400
 | Nat. Emittance [pm∙rad] | 61.57 (WO Ids), 52.55 (W 9 IDs)
 | Emittance coupling [%] | 10
 | Energy spread | 1.26E-3
 | Bunch Length(rms) [mm] | 3.6 (without HC) / 14.4 (with HC)
 | Lattice | Hybrid 7 Bend Achromat
 | Ring Circumference [m] | 799.297
 | Length of Straight Sections [m] | 6.06
 | Tune (H/V) | 68.18 / 23.26
 | (corrected) Chromaticity (H/V) | 5.8 / 3.5
 | Momentum compaction factor | 7.8 x 10-5
 | Number of buckets | 1332
 | Injection scheme | 4 Kicker bumps, off-axis, 2Hz
 | SR RF Parameter | Vaule
 | RF frequency [MHz] | 499.5935
 | RF Voltage [MV] | 3.5
 | Energy loss per turn [KeV] | 1098 (with 9 IDs: 1449)
SR Ring
SR RF
Beamline
Storage Ring
Booster
Linac
200 MeV
Photocathode
gun
01
02
03
04
C ~ 773 m
0.2-4 GeV
~ 11 nm
FODO lattice
Same tunnel

## Slide 5
Progress on 4GSR LLRF Prototype Development
RF Group
Pohang Accelerator Laboratory, POSTECH
January 26, 2026

## Slide 6
Introduction
Korea-4GSR RF system
Storage ring has total 10 of EU-HOM damped cavities
Booster ring has total 3 Petra-IV 5 cell cavities
Total 3 straight sections will be required for 10 cavities and 3 booster cavities
To place RF devices, including booster cavities, in one RF building, three booster cavities were places adjacent to the storage ring cavities.

## Slide 7
Introduction
Functional Requirements
RF amplitude & phase feedback loop (± 0.1% ± 0.1˚) - Control mode selection (Tone, GDR) - Amplitude & Phase set / readback - Amplitude & Phase offset set (Drift calibration) - PI control gain set / Readback - Gradient limit set (Clamp function) - Reference tracking - Monitoring feeder forward / reflect - Monitoring amplitude & phase error
Pulse generation - Pulse repetition rate - Pulse width
Frequency control - Detune angle calculation - Tuner detune angle offset set - Communication interface (ethernet, SFP+, Serial)
Interlock protection - Housekeeping function (LLRF status) - SSPA ready - External interlock - Cavity interlock (for fast interlock) - RF shutdown function
Ramping function - External trigger synchronize (BNC, LEMO, Optic interface) - Ramping profile generation
Field flatness control - Field flatness calculation (Cell #2 & Cell #4) - flatness window set - Communication interface (ethernet, SFP+, Serial)

## Slide 8
Introduction
Hardware architecture

## Slide 9
Digital processing flow
Reference tracking
Filed flatness control
Detune angle calculation
RF amplitude & phase feedback
Ramping / Pulse generation
Reflected power protection

## Slide 10
Implementation
LLRF Prototype
Pheobus GUI

## Slide 11
Performance test result
Intec | Open | Closed
Amplitude (%) | 0.0166 | 0.0158
Phase (deg.) | 0.03529 | 0.03503
Intec | Open | Closed
Amplitude (%) | 0.7904 | 0.0216
Phase (deg.) | 0.20654 | 0.03587
Intec | Open | Closed
Amplitude (%) | 1.1160 | 0.0264
Phase (deg.) | 0.21440 | 0.03627