## Slide 1: Introduction to PLS-II & PAL-XFEL
2026. 7. 6
Changbum Kim
Pohang Accelerator Laboratory

## Slide 2: Contents
Pohang Accelerator Laboratory (PAL)
Pohang Light Source-II (PLS-II)
PAL X-ray Free Electron Laser (PAL-XFEL)

## Slide 3: Accelerator Facilities in Korea
PLS-II and PAL-XFEL
KOMAC
RAON
KLS (Under construction)

## Slide 4: 국내 가속기 비교
종류 | 가속입자 | 주요활용목적 | 대표시설
방사광가속기 | 전자 | 물질의 미세구조 실시간 관측 | PLS-II, PAL-XFEL, KLS (오창)
중이온가속기 | 양성자보다 무거운 원소 이온 | 희귀 동위원소 생성, 우주 기원 탐구, 핵물리 | RAON (대전)
양성자가속기 | 양성자 | 물질 변형, 중성자 생성, 나노 바이오 연구 | KOMAC (경주)
중입자가속기 | 탄소 이온 | 암 치료 | 서울대병원 (기장)

## Slide 5: Pohang Accelerator Laboratory
PLS-II
PAL-XFEL

## Slide 6: 박태준 회장과 김호길 총장

## Slide 7: History of PAL

## Slide 8: Contents
Pohang Accelerator Laboratory (PAL)
Pohang Light Source-II (PLS-II)
PAL X-ray Free Electron Laser (PAL-XFEL)

## Slide 9: Layout of PLS-II

## Slide 10: PLS-II Electron Gun
PLS-II Thermionic Electron Gun
Circuit Diagram of Electron Gun

## Slide 11: Generation of Electron Beam (Thermionic Gun)
Thermal electron :
When the metal is heated hot, conduction band electrons escape from metal surface
I ~ T2e-W/kT
W : work function
* 1 eV ~ 11200 K

## Slide 12: Linear Accelerator (Basement Tunnel)
빔전송계(BTL)
Length: 180m
Thermionic electron gun
1 A, 10Hz pulsed beam
Norm. emittance: 150 µmrad
46 accelerating columns
3.0 GeV, full energy injection

## Slide 13: Linear Accelerator (First Floor)
2,856 MHz (S-band)
17 modulators (200MW, 7.5µs)
17 klystrons (80 MW, 4µs)
16 energy doublers (gain=1.5)

## Slide 14: Accelerating Structure
Klaus Wille, The Physics of Particle Accelerators: An Introduction

## Slide 15: Storage Ring

## Slide 16: PLS-II Lattice (Double Band Achromat)
Bend
Quadrupole
Sextupole
3.4 m
6.86 m
bx
by
hx

## Slide 17: Synchrotron Radiation

## Slide 18: Radiation

## Slide 19: Radiation from Circular Electron Motion

## Slide 20: Characteristics of Synchrotron Radiation

## Slide 21: Wavelength of Electromagnetic Wave

## Slide 22: Insertion Devices
I
I
I

## Slide 23: Superconducting RF Cavity

## Slide 24: Beamlines

## Slide 25: Imaging

## Slide 26: X-ray Lithography

## Slide 27: Structure Analysis

## Slide 29: Spectroscopy
Angle-Resolved Photoemission Spectroscopy

## Slide 30: 36 Beamlines in PLS-II
User Service: 190 days/year, Experiments: > 2000

## Slide 31: Contents
Pohang Accelerator Laboratory (PAL)
Pohang Light Source-II (PLS-II)
PAL X-ray Free Electron Laser (PAL-XFEL)

## Slide 33: First Ruby Laser

## Slide 34: PAL-XFEL Layout & Parameters
Undulator Line | HX | SX
Photon energy [keV] | 2.0 ~ 15 | 0.25 ~ 1.25
Beam Energy [GeV] | 4 ~ 11 | 3.0
Wavelength Tuning | Energy | Gap
Undulator Type | Planar | Planar
Undulator Period / Gap [mm] | 26 / 8.3 | 35 / 9.0
Self-seeding
  Main parameters
  e- Energy 11 GeV
  e- Bunch charge 20-200 pC
  Slice emittance < 0.4 mm mrad
  Repetition rate 60 Hz
  Bunch length 5 fs – 50 fs
  Peak current 3 kA
  SX line switching Kicker Magnet
30A
2 ps
200A
300fs
3kA
20fs
1kA
60fs

## Slide 35
Turner et. al., New J. Phys. 2008, 10, 053023
Milk Drop Coronet
by Harold E. Edgerton
The Horse in Motion
by Eadweard Muybridge
Ultra-fast Dynamics

## Slide 36: Long vs Short Exposure
www.thiot-ingenierie.com/en/2017/12/12/how-we-capture-the-invisible/

## Slide 38
Self-seeding
  Main parameters
  e- Energy 11 GeV
  e- Bunch charge 20-200 pC
  Slice emittance < 0.4 mm mrad
  Repetition rate 60 Hz
  Bunch length 5 fs – 50 fs
  Peak current 3 kA
  SX line switching Kicker Magnet
30A
2 ps
200A
300fs
3kA
20fs
1kA
60fs
PAL-XFEL Parameters
Undulator Line | HX | SX
Photon energy [keV] | 2.0 ~ 15 | 0.25 ~ 1.25
Beam Energy [GeV] | 4 ~ 11 | 3.0
Wavelength Tuning | Energy | Gap
Undulator Type | Planar | Planar
Undulator Period / Gap [mm] | 26 / 8.3 | 35 / 9.0

## Slide 39: Generation of Electron Beam (Photocathode RF Gun)
Photo-electron :
When a photon is absorbed by the metal surface, electrons can escape from metal surface
W ~ hν ~ Ebinding
(Cu work function: ~4.6 eV ~250 nm)

## Slide 40: Photocathode RF Gun

## Slide 41: Bunch Compressor
400 mm
Low E
High E
High E
Low E

## Slide 42: Pump Probe Experiment
Bragg intensity
XFEL
Optical Pump
Bi(111) thin film (50 nm) on GaSb(111)/Si(111)
X-ray: 6 keV
X-ray size: ~ 60 x 60 um2
Laser: 800 nm, 100 fs
Detector: MPCCD 0.5M
Bi (111) thin film
- No timing jitter correction
- averaged by 50 trials of the time delay scan and normalized by GaSb(111) Bragg peak intensity
- Only slow time-drift correction
- Vibration Frequency : 2.7 THz
- Instrument Response: 137 fs (FWHM)

## Slide 43
Ultra-high Resolution
2D Membrane Protein Crystallography

## Slide 44
Self-seeding
  Main parameters
  e- Energy 11 GeV
  e- Bunch charge 20-200 pC
  Slice emittance < 0.4 mm mrad
  Repetition rate 60 Hz
  Bunch length 5 fs – 50 fs
  Peak current 3 kA
  SX line switching Kicker Magnet
30A
2 ps
200A
300fs
3kA
20fs
1kA
60fs
PAL-XFEL Parameters
Undulator Line | HX | SX
Photon energy [keV] | 2.0 ~ 15 | 0.25 ~ 1.25
Beam Energy [GeV] | 4 ~ 11 | 3.0
Wavelength Tuning | Energy | Gap
Undulator Type | Planar | Planar
Undulator Period / Gap [mm] | 26 / 8.3 | 35 / 9.0

## Slide 45: Klystron & Modulator Gallery
Parameter | Unit | Value
Operation frequency | MHz | 2856
No. of Klystron, Modulator |  | 51
Max. repetition rate | Hz | 60
Operation pulse length | s | 4

## Slide 46: Linear Accelerator Tunnel
Parameter | Unit | Value
Energy | GeV | 10
Charge | pC | 200
No. of SLED |  | 42
No. of Acc. Column |  | 173

## Slide 47: Synchrotron Radiation

## Slide 48
High Brightness

## Slide 49
Self-seeding
  Main parameters
  e- Energy 11 GeV
  e- Bunch charge 20-200 pC
  Slice emittance < 0.4 mm mrad
  Repetition rate 60 Hz
  Bunch length 5 fs – 50 fs
  Peak current 3 kA
  SX line switching Kicker Magnet
30A
2 ps
200A
300fs
3kA
20fs
1kA
60fs
PAL-XFEL Parameters
Undulator Line | HX | SX
Photon energy [keV] | 2.0 ~ 15 | 0.25 ~ 1.25
Beam Energy [GeV] | 4 ~ 11 | 3.0
Wavelength Tuning | Energy | Gap
Undulator Type | Planar | Planar
Undulator Period / Gap [mm] | 26 / 8.3 | 35 / 9.0

## Slide 50: Undulators
Parameter | Unit | Value
No. of Undulator |  | 21
Length | m | 5
Period | mm | 26.0
Gap | mm | 8.3
Wavelength | nm | 0.1
Magnetic field | Tesla | 0.8124
K |  | 1.9727

## Slide 51: Electron Energy Change I
Brain McNeil, How an FEL Works

## Slide 52: Electron Energy Change II
Brain McNeil, How an FEL Works

## Slide 53: Electron Bunching I
Brain McNeil, How an FEL Works

## Slide 54: Electron Bunching II
Brain McNeil, How an FEL Works

## Slide 55
Microbunching Instability

## Slide 56: Radiation Power of Incoherent and Coherent Radiation
Brain McNeil, How an FEL Works

## Slide 57: Radiation Source & Intensity

## Slide 58
Coherent X-ray Diffraction Imaging
Highly Coherent
평양 5월1일 경기장
아리랑1호, 2호 위성영상

## Slide 60: Beamline
Experimental Station: Coherent X-ray Imaging, Hard X-ray Pump & Probe, Soft X-ray Pump & Probe

## Slide 62: XFELs in Operation

## Slide 63
Thank you for your attention!

## Slide 64: Future of XFEL
Energy Recovery Linac
XFEL Oscillator