## Slide 1: RAON Beam Dynamics
Dong-O Jeon
중이온가속기연구소
Institute for Basic Science
가속기여름학교 2026.07.08.

## Slide 2: Basic Concepts

## Slide 3: Lorentz equation
Lorentz equation governs the equation of motion of the beam.
Electric field or magnetic field is used to apply force to the beam.
Magnetic field multipoles are expressed as follows:

## Slide 4: Magnet Multipoles
Dipole Skew Dipole
Quadrupole Skew Quadrupole
Sextupole Skew Sextupole
N
S
N
S
S
N
N
N
N
S
S
S

## Slide 5: Dipole
Dipole is used to bend the beam.
Field is constant.
A standard technique for insulating magnet coils is to use epoxy resin, reinforced with fiberglass.

## Slide 6: Quadrupole
Quadrupoles are used to focus the beam transversely.
Field varies linearly.
However, focusing in one plane, defocusing in the other plane.

## Slide 7: Strong Focusing using quadrupoles
Transformation Matrix
L
Focusing is essential in accelerating beams.
Using focusing and defocusing quadrupoles, the net effect is focusing in both planes.  strong focusing

## Slide 8: Sextupole
Field varies quadratically.
Sextupoles are used to ensure that particles with slightly different energies or momenta are focused equally, preventing beam instability and particle loss in circular accelerators.

## Slide 9: Longitudinal Beam Dynamics
Longitudinal electric field Ez : both accelerating and focusing
Less acceleration when arrive early
More acceleration when arrive late
synchronous phase
synchronous particle

## Slide 10: Beam Emittance in Phase Space ~ beam quality
x
x’
Beam emittance is a measure of beam quality (roughly speaking phase space area).
RMS emittance is widely used for beam distributions.
rms emittance
X [mm]
x’ [mrad]

## Slide 11: RAON heavy ion accelerator

## Slide 12: Layout and Beam Parameters
RISP 4.3
High-precision
Mass Measurement Facility
RISP 4.6
Neutron Science
Facility
RISP 4.7
Bio-medical Research Facility
RISP 4.5
m-SR
RISP 4.1
Recoil Spectrometer (KOBRA)
Zero-Degree Spectrometer
RISP 4.2
Large Acceptance Spectrometer
RISP 4.4
Collinear Laser Spectroscopy
RISP 3.2
ISOL Facility
Low Energy Exp Bldg
High Energy Exp Bldg (A)
RISP 3.3
IF Facility
High Energy Exp Bldg (B)
 | Driver Linac |  |  |  | Post Acc. | Cyclotron
Particle | H+ | O+8 | Xe+54 | U+79 | RI beam | proton
Beam energy (MeV/u) | 600 | 320 | 251 | 200 | 18.5 | 70
Beam current (pμA) | 660 | 78 | 11 | 8.3 | - | 1000
Power on target (kW) | > 400 | 400 | 400 | 400 | - | 70

## Slide 13: Accelerator Systems

## Slide 14: RAON heavy ion accelerator
Campus Area: 952,066 m2

## Slide 15: Injector
There are 28 GHz and 14.5 GHz ECR Ion Sources to generate ions.
LEBT (Low Energy Beam Transport) is to transport and match the beam from the ECR-IS to the RFQ (Radio-Frequency Quadrupole).
81.25 MHz RFQ (10 keV/u to 500 keV/u)
Medium Energy Beam Transport is to transport and match the beam from the RFQ to the SCL (Super-Conducting Linac)
SCL

## Slide 16: ECR Ion Source (Electron Cyclotron Resonance)
ECR ion source is to generate charged ions from gas or metals.
High performance ECR ion source is needed to generate high charged beams.
Performance
High intensities
High charge states
Increase the ECR frequency to increase the plasma density
Present state
- 28 GHz Superconducting ECR IS: US, Japan, China, Korea
ωce = qe B / Me = ωHF
B axial
B radial
Minimum B
+
=
18 GHz
28 GHz
ne ωrf2 qopt  log B
neTe ion  B
we = = wrf
e•B
m
Resonant electron heating

## Slide 17: 28 GHz ECR Ion Source
Plasma is produced and heated by microwave.
Plasma is confined by minimum B structure. (solenoids + sextupoles)
To produce highly charged or high current ion beams need high ne (electron density) and long Tion (ion confinement time)
➔ high ωRF ➔ high B-field
28-GHz ECR IS needs B ~ 3.5T and requires superconducting magnets.

## Slide 18: ECR IS Design Parameters
Frequency (GHz) | 28 + (18)
RF Power (kW) | 10
Plasma Chamber Diameter (mm) | 150
Plasma Chamber Material | Aluminum
Mirror Length (mm) | 500
Vext (kV) | 30
SC Wire | NbTi
Number of Solenoid Coils | 4
Sextupole Winding Type | Saddle
Binj (T) | 3.5
Br (T) | 2
Bext (T) | 2
Bmin (T) | 0.4 ~ 0.8

## Slide 19: 28-GHz ECR Ion Source
총 7대의 cryocooler 사용
2단 냉동기 6대, 1단 냉동기 1대
재응축형으로 운전
항 목 |  |  | 단 위 | 사 양
Outside Diameter of Cryostat |  |  | mm | 898
RT bore if Cryostat |  |  | mm | 170
Material of Cryostat |  |  | mm | STS
Length of Cryostat |  |  | mm | 1714
Weight of Cryostat(iron york제외) |  |  | kg | <1600kg
Vacuum Rate of Cryostat |  |  | torr | <~9x10-5
He Leak Rate of Cryostat |  |  | mbar.l/sec | <~9x10-9
LHe Vessel | Volume |  | liter | <1000
 | Outer Dimeter |  | mm | 740
 | Inner Diameter |  | mm | 195
 | Heater |  | W | 25
Top plate | Number of CL | 500A CL | pair | 1
 |  | 300A CL | pair | 4
 | Electrical feedthrough |  | ea | 3
 | LHe Transfer & safety & vent port |  | ea | 1
 | Relief valve |  | ea | 1
 | Rupture disk |  | ea | 1
냉동기 (6대) RDK-415 | 1단 (50K) |  | W | 300
 | 2단 (4.2K) |  | W | 9
냉동기 (1개) RDK-400 | 1단 (40K) |  | W | 74
Number of HTS CL | 500A Current Lead |  | pair | 1
 | 300A Current Lead |  | pair | 4
Number of 60K Thermal Shield |  |  | layer | 1
Number of Cooler Port |  |  | ea | 6
Binj= 3.5 T, Bext= 2.2 T,
Br= 2 Becr , Bmin= 0.7 T

## Slide 20: Sextupole of ECR IS
The comparison between the racetrack type and the saddle type
Saddle type
Racetrack type

## Slide 21: Sextupole Prototypes
Saddle type
Racetrack type

## Slide 22: Low Energy Beam Transport (LEBT)
[SCL1 LEBT layout (TDR) ]
[SCL3 LEBT layout (TDR) ]
LEBT layout (TDR)
- SCL1 LEBT: 180° bending (Uranium beam)
- SCL3 LEBT: 90° bending (RI beam)
Present LEBT layout (Uranium, RI beam)
- 180° bending
[ Present LEBT layout ]
28 GHz ECR IS

## Slide 23: ESQ (Electro-Static Quadrupole)
Electro-Static Quadrupole (ESQ) is used for transverse focusing in the LEBT.
Force is independent of particle velocity.

## Slide 24: LEBT beam dynamics (28-GHz ECR IS)
LEBT functions
- charge selection (selecting U 33+, 34+)
- first order achromat design
- chopping
[ Achromat design ]
[ TRACK simulation : charge selection ]

## Slide 25: LEBT beam dynamics (14.5-GHz ECR IS)
25
LEBT functions:
- charge selection
- first order achromatic design
- chopping
[ Achromat design ]
[ 14.5GHz ECR IS ]
[ TRACK simulation : charge selection ]
[ 28GHz ECR IS ]

## Slide 26: Multi Harmonic Buncher (MHB) & Velocity Equalizer (VE)
reduces RFQ output beam longitudinal rms emittance,
MHB uses 3 harmonics : 40.625 MHz, 81.25 MHz, 121.875 MHz,
separating U 33+ and 34+ beam,
making input energy equal and inject to RFQ.
U34+
U33+
Before MHB
After MHB
After VE
Before RFQ

## Slide 27: Operation without MHB
MHB (Multi Harmonic Buncher) & VE (Velocity Equalizer) are very essential to FRIB RFQ design
FRIB RFQ transmission 80%
RAON RFQ employs shaper and gentle buncher. So MHB & VE are not essential.
RAON RFQ transmission 98%
We studied whether beam operation is feasible without MHB through machine imperfection study.
Longitudinal Emittance | with MHB, VE (keV/u-ns) | without MHB, VE (keV/u-ns) | Change (%)
RMS emittance | 0.380 | 0.916 | 141% increase
99.9% emittance | 14.92 | 15.70 | 5% increase

## Slide 28: RFQ comparison
FRIB
FRIB RFQ
Accelerates from 12keV/u to 500keV/u
Less adiabatic bunching
Cuts off 20% of the beam
Transmission is low ~80%
Z emittance is small n,rms : 0.08 keV/u-ns
εnz,99.5 % : 1.3 keV/u-ns
Segment1 acceptance
RAON
RAON RFQ
Accelerates from 10keV/u to 500keV/u
Adiabatic bunching
Transmits almost all the beam
Transmission is high ~98%
Z emittance is big n,rms : 0.91 keV/u-ns
εnz,99.5 % : 8.5 keV/u-ns
SCL3 acceptance
~27 keV/u-ns
~30 keV/u-ns

## Slide 29: Operation possible without MHB
Machine imperfection studies show that 400 kW operation is possible without MHB and VE for the RAON.
End-to-end machine imperfection study showed that beam loss requirement < 1 W/m is met.
P2DT
collimators

## Slide 30: RFQ Radio Frequency Quadrupole
Perfect link between ion source (DC beam) and linac (bunched beam).
Bunches and accelerates DC input beam into a bunched beam  reduces beam loss dramatically.
Accelerate high current and small emittance beam to reasonably high energy.

## Slide 31: RFQ history
1970 Kapchinskij and Teplyakov proposed the idea of the radiofrequency quadrupole (I. M. Kapchinskij and V. A. Teplvakov, Prib. Tekh. Eksp. No. 2, 19 (1970)).
1974 experimental test of K&T idea at USSR Institute for High Energy Physics in Protvino. A 148.5-MHz RFQ accelerated 100-KeV protons to 620 KeV with a transmission of 50%.
1977 RFQ concept is published in the western world. Strong interest in Los Alamos National Laboratory (USA). Decision to test the RFQ principle for possible application in development of high current low emittance beams. Developments of computer codes for RFQ design.
1979 Start of P.O.P. (Proof-of-principle experiment) at Los Alamos. 425 MHz RFQ accelerates a 100-keV proton beam to 640 keV with a transmission of 90%, as predicted by the codes. (1980.02.14.)
Nowadays hundreds of RFQ accelerators are operating in the world.

## Slide 32: RFQ
Proton is accelerated to a few MeV
and heavy ions to < 1 MeV/u

## Slide 33: RFQ four-vane type or four-rod type
four-vane type
Frequency depends on cylinder dimension
Need dipole mode stabilization
vane
rod
four-rod type
Easy to machine
Problems with end cells
Less efficient than four-vane type

## Slide 34: RFQ design parameters
PARAMETER | VALUE
Beam Properties: | 
Frequency | 81.250 MHz
Particle | H+1 to U238+33
Input Energy | 10 keV/u
Input Current | 0.4 mA
Input Emittance: transverse (rms, norm) | 0.012 .cm. mrad
Output Energy | 0.507 MeV/u
Output Current for 0.4mA in. | ~0.39 mA
Output Emittance: transverse (rms, norm) longitudinal (rms) | 0.0125 .cm. mrad ~26 keV/u-Degree
Transmission | ~98 %
Structures and RF: | 
Peak surface Field | 1.70 Kilpatrick
Structure Power (for U238+33) | 92.4 kW
Beam Power (for 0.2mA each U238+33&+34) | 1.44 kW
Total Power | 94 kW
Duty Factor | 100%
RF Feed | 1 Drive loops
Mechanical: | 
Length | 4.94 meter
Operating Temperature | TBD Degree C
RFQ accelerates and bunches the CW beam from the ECR ion source.
X-Xp
Y-Yp
f-E
X
Y
f
E

## Slide 35: RFQ Beam Dynamics RAON
s0t and s0l
(transverse and longitudinal focusing)
along the RFQ
Transverse and longitudinal
rms emittances along the RFQ
transverse
longitudinal
s0t
s0l

## Slide 36: RFQ design
- 4940.07 mm
- 9 Modules
- each ~547 mm long
- alternating slug and vacuum port
- 12 Vacuum Ports
- 20 Tuner Ports
- 10 Pickup Ports
- 2 Coupler Ports
4 x pickup
4 x pickup
2 x RF coupler
2 x pickup

## Slide 37: Cooling channel
Coolant temperature 20
Coolant temperature 20
Cooling channel
HE

## Slide 38: EM & Thermal design
With tuner : 81.26 MHz
Tuner insertion depth
: 60 mm
Max : 60.15
@ dummy
Operating temperature: 30°

## Slide 39: RFQ prototype and fabrication
RFQ Engineering Design (2013.08)
Design review (2013.11)
RFQ Prototyping
RFQ prototype completed successfully through domestic vendor (2014.10)
RFQ contract awarded (2015.04)
RFQ fabrication completed through domestic vendor (2016.08)
RFQ
prototype
RFQ
prototype

## Slide 40: NDPS requires single bunch beam
NDPS (Nuclear Data Production System) requires single bunch beams with < 1 MHz from the SCL3.
This requires a very fast chopper system in the MEBT that consists of a chopper and a beam stop.
The following slides show the requirement for the NDPS and the MEBT is modified according to the requirement.

## Slide 41: Medium Energy Beam Transport (MEBT)
MEBT Layout (TDR)
- SCL1, SCL3 MEBT: 2 Normal Conducting QWR type buncher cavity
- SCL1 MEBT: 1-m space for bending magnet
[ MEBT layout for SCL1 ]
[ MEBT layout for SCL3 ]
Present Layout
- Lattice modified to accommodate the single bunch selector
* 4 Bunchers, 11 Quadrupoles
[ Present MEBT layout for SCL3 ]

## Slide 42: MEBT of SPIRAL2 (France)
2008, Giacomo, DESIGN OF THE MEBT REBUNCHERS FOR THE SPIRAL2
Total length of MEBT = 7.5 m
0.75 m
0.40 m

## Slide 43: Modified MEBT
The modified MEBT requires additional 3 quadrupoles and 1 buncher.
The distance between the chopper and the beam stop is 2.41 meter.
The length changes from 5640 mm to 6450 mm (810 mm increase).
The modified MEBT was configured to minimize the beam size along the MEBT.
2.41 m
chopper
beam stop
SCL3
X beam size
Y beam size

## Slide 44: RAON Superconducting Linac

## Slide 45: Advantages of Superconducting Linac
Higher electric field gradient can be achieved than normal conducting linac.
Practically all the rf power can be used to accelerate beams, due to practically zero power dissipation to the cavities (superconducting).
Construction and operating costs are less compared with the normal conducting linac.
The large bore of the SC cavity reduces linac component activation due to beam loss.
One cavity type can accelerate wide range of velocities.
In case of RAON, four cavity types are used to accelerate from 0.5 MeV/u to > 200 MeV/u.

## Slide 46: SCL design principle
SCL (Super-Conducting Linac) is to accelerate various ion beams from light ions to heavy ions with 400 kW target beam power.
Beam loss is kept under 1 W/m for hands-on maintenance.
Cavity types have been selected that are optimal for the corresponding beam velocity.
SCL should be designed anticipating beam power increase in the future.

## Slide 47: SCL design principle
RAON’s linac lattice design, cryomodule and cavity design are carefully chosen to avoid the following potential issues
Issues and operation complications due to 8T solenoids next to SC cavities in cryomodules,
Alignment of solenoids in cryomodules,
SC cavity RF design issues of detachable bottom plates.
Maximize cavity apertures to reduce the risk of cavity damage by beam loss: QWR, HWR cavities (aperture 40 mm), spoke cavities (aperture 50 mm).
Beam diagnostics and collimation are flexible with the RAON design.

## Slide 48: Quarter Wave Resonator (QWR)
48 ≤ f ≤ 160 MHz, 0.001 ≤ b ≤ 0.2
Compact, Modular, High performance, Low cost, easy access
Dipole steering, Mechanical Stability, Quadrupole components
CEA QWR b=0.07
88 MHz
FRIB QWR b=0.085
161 MHz
TRIUMF HWR b=0.07
106 MHz

## Slide 49: Half Wave Resonator (HWR)
160 ≤ f ≤ 352 MHz, 0.09 ≤ b ≤ 0.3
No dipole steering, Lower Ep than QWRs, Wide beta range
Not easy access, difficult to tune, Less efficient than QWR, Quadrupole components
INFN HWR b=0.17
352 MHz
SARAF HWR b=0.09
176 MHz
ANL HWR b=0.26
172.5 MHz

## Slide 50: HWR choice
QWR cavities are not suitable for high intensity beam acceleration.
Many high intensity accelerators opt for HWR cavities.
IFMIF, PIP-II (Fermilab), CiADS (China) employ HWR cavities:
IFMIF : RFQ + HWR (deuteron 125 mA)
PIP-II (Fermilab) : RFQ + HWR + SSR (proton 25 mA)
CiADS (China) : RFQ + HWR + SSR (proton 10 mA)
RAON employs HWR cavity following a short QWR section, enabling high-intensity beam acceleration in the future and keeping away from dipole field kicks of QWR.

## Slide 51: Choice of geometric beta (2012)
RAON: 0.047, 0.120, 0.30, 0.53
FRIB: 0.041, 0.085, 0.29, 0.53
QWR
HWR
SSR1
SSR2
For U beam

## Slide 52: Superconducting Cavity
Parameters | Unit | QWR | HWR | SSR1 | SSR2
bg | - | 0.047 | 0.12 | 0.30 | 0.51
F | MHz | 81.25 | 162.5 | 325 | 325
Aperture | mm | 40 | 40 | 50 | 50
QRs | Ohm | 21.3 | 41.6 | 97.6 | 112
R/Q | Ohm | 470 | 305 | 230 | 296
Vacc | MV | 1.1 | 1.5 | 2.5 | 4.1
Epeak | MV/m | 35 | 35 | 35 | 35
Bpeak | mT | 57 | 55 | 58 | 64
Qcalc/109 | - | 2.1 | 4.2 | 9.0 | 10.5
Temp. | K | 4.5 | 2 | 2 | 2
(Epeak = 35MV/m)
Prototype cavities fabricated through domestic vendors (2014)

## Slide 53: QWR prototype test (2014.12) Tested in collaboration with TRIUMF
Operating point
QWR designed by the IBS, fabricated by domestic vendors met the specification, tested at the TRIUMF.
QWR achieved 160% of design at 4K test.
QWR achieved 210% of design at 2K test.
Field Emission
LFD | -19.8 Hz/(Mv/m)2
df/dp | -42.9 Hz/Torr
BCS | 0.14 n (2K) 4.7 n (4K)
Residual | 2.5 n

## Slide 54: HWR prototype test (2014.12) Tested in collaboration with TRIUMF
The prototype met the specification and achieved more than 200% of design field at 2K,
Need to improve the Q factor at 2K
Design change to remedy the multipacting band near the operating point.
LFD | -8.8 Hz/(Mv/m)2
df/dp | -10.8 Hz/Torr
BCS | 0.11 n (2K) 9.8 n (4K)
Residual | 16.8 n

## Slide 55: Driver SC Linac Lattice
NC quadrupole
SCL
with SC solenoids
SCL
with NC doublets
QWR
HWR
Design to accelerate high intensity heavy ion beams
Flexile operation to meet the needs of various user groups
beam box

## Slide 56: Machine imperfection study (2012)
Max. envelope
Centroid
Emittance
baseline
solenoid
10% increase
130% increase
76% increase
350% increase
The shade region represents the bounds of envelope, centroid and emittance due to misalignment and field errors.
The apertures of quadrupole and solenoid are 40 mm.

## Slide 57: RAON SCL Layout
collimator
quadrupole
cryomodule
SCL layout provides good beam diagnostics configuration for machine tuning.
Necessary beam diagnostics can be installed at beam boxes.
Enables flexible beam loss collimation configuration, improving beam quality for users, reducing beam loss.
Beam
beam box

## Slide 58: SCL cryomodule design
FRIB cryomodules contain both cavities and solenoids
RAON cryomodules contain cavities only and quadrupoles are outside
FRIB cryomodule
RAON cryomodule
solenoid
quadrupole

## Slide 59: Solenoid issues in cryomodules
FRIB
8T solenoids in a cryomodule
Can magnetically pollute the environment
FRIB cavity is exposed to ~15 G fringe field
need local 4K magnetic shield for cavities
Can degrade cavity performance during quench through trapped flux
Must use non-magnetic materials (even bolts and nuts) inside cryomodules
Solenoid magnetic shield can be magnetized
RAON
Quadrupoles outside a cryomodule
No magnetic pollution of the cryomodule environment
Achieving B field < 15 mG is not an issue
Conventional magnetic shield is enough
Cavity performance is not affected
Materials inside cryomodules not issue

## Slide 60: Alignment & Tuning
FRIB
Alignment of superconducting solenoids is not trivial
Solenoids in a cryomodule experiences ~3 mm shift during cool-down to 4K
FRIB is aiming at 2 RMS < ±1.0 mm alignment error
Misalignment of solenoids causes emittance growth and beam loss
When cavity or solenoid quench happens, turn-on procedure is very complicated
Beam loss can cause solenoids to quench
RAON
Alignment of quadrupoles is not an issue
Quadrupole alignment is independent of cryomodule cool-down
Quadrupoles can be aligned < ± 0.15 mm with ease
Emittance growth from quadrupole misalignment can be easily controlled
When cavity quench happens, turn-on procedure is simple
More suitable for high power beam acceleration beyond 400 kW

## Slide 61: Beam Dynamics
Baseline design of the SCL3, Charge Stripper Section and SCL2, HEBT was done.
End-to-end beam dynamics simulations were done for the entire linac.
Transfer line of P2DT was designed for charge separation/selection.
Machine imperfection studies were done.

## Slide 62: SCL3 beam dynamics
lattice
- HWR A type 13 cryomodules, HWR B type 19 cryomodules
 | input | output | 증가(%)
x | 0.134 | 0.136 | 1.7
y | 0.132 | 0.135 | 2.6
Long. | 0.917 | 1.150 | 25.4
[ rms emittance 증가 ]
Transverse: mm-mrad
Longitudinal: keV/u-ns
Transverse
Longtudinal

## Slide 63: P2DT layout
[ TDR P2DT Layout ]
[ Present P2DT Layout ]
P2DT selects and transports Uranium beam 5 charge states
Quadrupole magnets reduced: 26  18
Sextupole magnets added: 8
bunchers
bunchers

## Slide 64: P2DT beam dynamics
lattice features:
- Isochronous design
- 2nd order achromatic design
Uranium beam distributions
at beam selection location
 | input | output | Increase (%)
x | 0.165 | 0.176 | 7.0
y | 0.158 | 0.161 | 1.8
Long. | 1.164 | 1.278 | 9.9
[ rms emittance increase (5Q) ]
+77
+78
+79
+80
+81

## Slide 65: P2DT Diagnostics & Collimation
DN63 FVs are located where beam sizes are relatively small.

## Slide 66: P2DT Diagnostics & Collimation
Beam diagnostics configuration has been identified.
Beam collimation positions are identified to control the beam loss to the buncher cryomodules and to SCL2.
Collimators should meet the following:
water-cooling up to 100 W,
adjustable depth (with independent actuators),
should have ports for X and Y collimators.

## Slide 67: Mismatch induces halo formation
Matching is essential, as the beam enters the next section of a linac.
Mismatch has long been known as a source of halo formation.
establish matching as best as one can
Envelope instability and 4th order resonance manifest when zero-current phase advance is above 90°. keep the phase advance below 90°
Matched
beam
Mismatched
beam

## Slide 68: Start-To-End Beam Dynamics (SCL3-P2DT-SCL2)
After SCL3
After P2DT
After SCL2
132Sn+20 → 132SN+45
0.5 MeV/u → 183.6 MeV/u
Zero-current phase advances are kept below ~100° to avoid 4th order space-charge resonance and envelope instability.

## Slide 69: Start-to-end simulation (238U33+,34+ : 28GHz → SCL2)

## Slide 70: Start-to-end simulation (132Sn33+ : ISOL → SCL2)

## Slide 71: Start-to-End Beam Dynamics Uranium
 | QWR | HWR |  | STRIP | SSR1 | SSR2
CM (mm) | 450 | 1400 | 2720 |  | 2216 | 5600
GV/CM/GV (mm) | 620 | 1570 | 2890 |  | 2386 | 5770
WS (mm) | 590 | 670 | 670 |  | 820 | 820
1 period (mm) | 1210 | 2240 | 3560 |  | 3206 | 6590
length (m) | 26.6 | 29.1 | 49.1 | 27.9 | 67.3 | 118.6
linac length (m) | 26.6 | 55.7 | 105.6 | 133.5 | 200.8 | 319.4
# of periods | 22 | 13 | 19 |  | 23 | 23
# of cavity per period | 1 | 2 | 4 |  | 3 | 6
# of cavities | 22 | 26 | 76 |  | 69 | 138
energy (MeV/u) | 2.5 | 7.4 | 18.5 |  | 68.0 | 206.8

## Slide 72: Start-to-End Beam Dynamics Proton
 | QWR | HWR |  | STRIP | SSR1 | SSR2
CM (mm) | 450 | 1400 | 2720 |  | 2216 | 5600
GV/CM/GV (mm) | 620 | 1570 | 2890 |  | 2386 | 5770
WS (mm) | 590 | 670 | 670 |  | 820 | 820
1 period (mm) | 1210 | 2240 | 3560 |  | 3206 | 6590
length (m) | 26.6 | 29.1 | 49.1 | 27.9 | 67.3 | 118.6
linac length (m) | 26.6 | 55.7 | 105.6 | 133.5 | 200.8 | 319.4
# of periods | 22 | 13 | 19 |  | 23 | 23
# of cavity per period | 1 | 2 | 4 |  | 3 | 6
# of cavities | 22 | 26 | 76 |  | 69 | 138
energy (MeV/u) | 7.5 | 34.2 | 87.4 |  | 222.2 | 630.0

## Slide 73: Machine imperfection study
Accelerators include a certain level of imperfections.
End-to-end machine imperfection studies were done.
All the imperfections were taken into consideration:
Uranium 33+ and 34+ beams using the TRACK code
Macro-particle numbers : 50k + 50k
Number of seeds : 100
Input beam was generated with initial waterbag beam by tracking from the LEBT to the RFQ
imperfections | values | type
quad displacement | ± 0.15 mm | uniform, peak-to-peak
quad rotation | ± 5 mrad | uniform, peak-to-peak
cavity displacement | ± 1 mm | uniform, peak-to-peak
cavity rf amplitude | ± 1 % | 3σ truncated Gaussian, peak-to-peak
cavity rf phase | ± 1° | 3σ truncated Gaussian, peak-to-peak

## Slide 74: 400 kW beam operation possible
Beam loss < 1 W/m is observed at SCL2 transition with updated cavities.
When all the cavities are operating, 400-kW beam operation is feasible.
Even without orbit correction, 1 W/m beam loss requirement is met.
SCL3
SCL2
P2DT
without Orbit Correction
SCL3
SCL2
P2DT

## Slide 75: Beam Commissioning

## Slide 76: Accelerator Systems Low Energy Superconducting Linac (SCL3)
Cryomodule(CM) & Warm section was assembled in the clean booth at tunnel
Total Particle counts < 30 counts / 10 min (size > 0.5um)
Warm section
CM
CM
CM
SCL3

## Slide 77: Beam Commissioning
Measurements for commissioning
Emittance (X and Y) : Allison scanners, wirescanners, quad scan methods
Cavity RF set-point (phase scan, BPM)
Beam energy (phase scan, TOF with BPMs)
Beam current, transmission (ACCT, FC)
Orbit correction (BPM / Wirescanner & dipole steerer)
Beam transverse profile (wirescanner)
Beam longitudinal profiles (Fast Faraday Cup)
Transverse matching (wirescanner)
Physics applications for commissioning
BIPAM (Beam Input Parameters And Matching)
CAPS (Cavity Amplitude and Phase Scan)
Orbit correction application
Emittance data analysis & wirescanner data analysis
77

## Slide 78: The RAON Injector
- RAON injector: 14.5 GHz ECR IS (10keV/u), LEBT, RFQ (507 keV/u) , MEBT
- Injector beam commissioning: Ar9+, Ar8+, O6+, Ne4+, Ne6+, He2+, H+ beams
QWR

## Slide 79: LEBT beam parameters
Beam parameter measurement (Allison scanners, wire-scanners)
- measuring emittances, beam sizes, beam parameters
controlling beam optics
Emittance measurement (Allison scanner, beam size fitting, quad scan)
Beam size fitting method
Beam emittance
(Allison scanner)
 | X | Y
Allison | 0.048 | 0.067
Quad Scan | 0.041 | 0.038
emittance comparison
Quad scan
(beam emittance)

## Slide 80: LEBT beam measurements for various beams
- By using the Allison data and wirescanner data, we established beam matching to RFQ.
- Beam dynamics: using TRACK or DYNAC codes
Initial Allison scanner result of Ne4+
After adjusting quadrupoles for Ne4+
TRACK results after beam matching to RFQ

## Slide 81: Experiment vs Simulation (LEBT)
- We compared WS data with TRACK simulation in LEBT
* TRACK input: calculated from Allison emittance data
* In general, TRACK simulations and WS data are in good agreement
with each other.
Ne4+
Ar9+
He2+
Ar8+
J.H. Jang

## Slide 82: LEBT beam parameters: beam size fitting
O6+ 48uA
injector transmission: 90%
LEBT
RFQ
Beam parameters are measured by fitting the beam size or by emittance scan.
Beam optics is controlled.
Matching can be performed.
LEBT
RFQ
Ar8+ 50uA
injector transmission: 95%
X beam size
Y beam size
H+ 98uA
LEBT transmission: 97%
LEBT
RFQ

## Slide 83: H+ beam in LEBT
The H+ beam displays large emittances and strong beam tails.
X emittance displays extended tails. So the beam is collimated.
Beam transmission in the LEBT is 97%.
ex=0.105 mm-mrad
ey=0.189 mm-mrad

## Slide 84: RFQ set-point
RFQ transmission: (ACCT in LEBT and ACCT in MEBT)
RFQ transmission is greater than 90%.
RFQ transmission is low for Ne beams due to tails
 We can improve it by using the slits in LEBT
 | Ar9+ | Ar8+ | Ne4+
Transmission | 93.4% | 95.4% | 85.7%
Set value | 51.5 kW | 62.9 kW | 67.4 kW
MEBT
RFQ set-point for Ar9+
RFQ set-point for Ne4+
RFQ set-point for Ar8+

## Slide 85: Matching Ar8+ beam to RFQ
The following are crucial in order to achieve good beam quality
matching to the RFQ
on-axis injection to the RFQ
Beam profiles are almost Gaussian.
MEBT wirescanners
85
WS1
WS2
WS3

## Slide 86: On-axis injection to RFQ
ex=0.086 mm-mrad
ey=0.064 mm-mrad
ex=0.114 mm-mrad
ey=0.068 mm-mrad
ex=0.098 mm-mrad
ey=0.146 mm-mrad
X kick
Y kick
reference
Jeon et al, NIM A 1052, 168250 (2023)
On-axis injection to RFQ is crucial: Off-axis injection increases output beam rms emittances and beam tails.
86

## Slide 87: MEBT beam emittance
MEBT beam parameter measurements:
using wire-scanners
beam parameters used for matching to SCL3
Beam size fitting method and quad scan show consistent results.
quad scan technique takes rather long time
Beam size fitting requires single scan of wire-scanners
X plane
Y plane
Quad scan
 | ex mm-mrad | ey mm-mrad
Beam size fitting | 0.068 | 0.044
Quad Scan | 0.064 | 0.049
emittance comparison
WS data
Beam size fitting

## Slide 88: Experiment vs Simulation (MEBT)
- Adjust RFQ output beam parameters
by using WS results.
- Compare TRACK simulation and 3 WS data
* Different results between TRACK simulation
and WS data  Adjust RFQ output beam
rms beam size through MEBT
Ar9+
Ne4+
He2+
Ar8+
J.H. Jang

## Slide 89: Matching between sections (Ar8+)
Matching between linac sections are demonstrated with four quadrupoles:
MEBT to QWR
QWR to HWRA
MEBT to QWR matching
QWR to HWRA matching
MEBT
QWR
QWR
HWR
X beam size
Y beam size
X beam size
Y beam size

## Slide 90: Simulation reveals hardware issues
Comparison with simulations identifies problems.
Inconsistency in Y-plane turned out to be MEBT QM09 power-supply.
Large discrepancy between MEBT QM09 set value and readback value  turned out to be Power Supply issue
readback value
set value
MEBT
QWR
MEBT
QWR

## Slide 91: Ar8+ beam in the LEBT and in the SCL3
LEBT
RFQ
Ar8+ 45uA
injector transmission: 95%
MEBT
SCL3(QWR)
ex=0.091 mm-mrad
ey=0.063 mm-mrad
ex=0.059 mm-mrad
ey=0.033 mm-mrad
91
X beam size
Y beam size
X beam size
Y beam size

## Slide 92: SCL3 Diagnostics and Phase Scan
For RF set-point, phase scan technique is used to set the RF set-point.
92
cryomodule
quadrupole
beam box

## Slide 93: Phase Scan
RF set-points of superconducting cavities are set by phase scan technique using two BPMs.
Phase scan determines cavity RF amplitude & phase, input & output beam energy.

## Slide 94: Beam Commissioning of SCL3
First Beam commissioning with 40Ar+9 beam: 1Hz, 100 sec
- Sep. 2022: Start cool-down
- Oct. 2022: Cool down to 4.5K finished
- Oct. 2022: Beam commissioning with initial 5 cavities of QWR finished
- Dec. 2022: QWR beam commissioning finished
- Jan. 2023: Cool down to 2K finished
- May 2023: SCL3 beam commissioning finished
* 10 cavities (out of 124) were not used due to control issues, cold leak, etc.
* Accelerating fields: QWR < 5 MV/m (design 6.1 MV/m), HWR < 4 MV/m (design 6.6 MV/m)
- June 2023: KoBRA beam test (May 30 ~ June 2)
Second Beam commissioning with 40Ar+8 beam: 1Hz, 100 sec
- March 2024: Cooled down to 2K
- April 29, 2024: SCL3 beam commissioning started
* 8 cavities are excluded for similar reasons
* Accelerating fields: QWR < 5 MV/m (design 6.1 MV/m), HWR < 5 MV/m (design 6.6 MV/m)

## Slide 95: BPM phase jitters improved
Cavity RF set-points are obtained by phase scan technique using 2 BPMs.
In 2024, BPM phase jitters are reduced compared with the 2023 run.
Beam phase jitter is still large and tighter LLRF control is necessary.
Last HWR cavity (2024)
Last HWR cavity (2023)
95

## Slide 96: 2024 Ar8+ beam commissioning
3 QWR cavities were turned off.
5 HWR cavities were turned off.
RF set-points of near-by cavities were adjusted to minimize beam loss.
Cavities were set using phase scan:
beam energy: 18.53 MeV/u
Beam transmission ~ 93%.
Energy discrepancy observed (phase scan vs dipole) → Now BPM calibration is done and cross-checking with dipole will be performed.
96

## Slide 97: Beam energy is consistent (2026) phase scan vs dipole scan
BPM calibration enables to determine the input beam energy with an accuracy of tens of keV/u.
40Ar8+ beam energy : 18.92 MeV/u (phase scan),
18.71 MeV/u (dipole scan)
22Ne6+ beam energy : 24.05 MeV/u (phase scan),
24.47 MeV/u (dipole scan)
2026 campaign 40Ar8+
Typical phase scan result

## Slide 98: SCL3 beam transmission
- Beam transmission through SCL3:
ACCTs in MEBT and in P2DT beam line
- Beam transmission: < 70% in 2023, ~93% in 2024.
- Orbit correction is important, but there is more beam
loss than expected.
[ SCL3 Transmission (2023) ]
[ SCL3 Transmission (2024) ]
[ Transmission before and after orbit
correction (2024) ]
Orbit correction

## Slide 99: Beam Loss & Longitudinal Acceptance
Longitudinal Acceptance: Important factor to beam loss.
Off cavities reduce acceptance and increase beam loss.
Error Analysis: Beam loss can be described qualitatively.
[ All cavities ON ]
[ 8 cavities OFF ]
[ QWR3 revived ]
[ QWR3,12 revived ]
Longitudinal
Acceptance
Beam Loss

## Slide 100: Phase Space Tomography

## Slide 101: Tomography
Tomography is an advanced imaging technique that creates cross-sectional slices of a three-dimensional object.
Instead of a single projection like a traditional X-ray, tomography involves taking multiple measurements from different angles around the subject. A computer then processes these measurements using mathematical procedures to assemble a complete 3D volume made up of individual slices.
Tomography technique has been applied to particle accelerators to reconstruct beam distribution in phase space from multiple profile measurements.

## Slide 102: Hybrid tomography method
Tomography reconstruction has been applied to cases where emittance scanner is not available (due to space limitation or high beam energy).
Most tomography method is based on linear mapping.
However, sometimes it is needed to include nonlinearities such as space charge effect, optical nonlinearities.
Space charge effect is self field effect of charged particle beams.
102

## Slide 103: Hybrid tomography method
At CERN, a hybrid tomography method was developed, utilizing the beam dynamics code Travel that include the space charge effect and nonlinearities.
Dimov et al, HB2016
103

## Slide 104: Tomography in the MEBT
Tomography reconstruction was applied to get the RFQ output beam distribution using the 4 wire-scanners in the SCL.
Wire-scanners are located at optically periodic positions.
Phase advances between two consecutive wire-scanners are 87° ~ 80°.
104
beam

## Slide 105: Measurement vs. Tomography (SCL wire-scanners)
Tomography reconstruction manifests excellent agreement between the measurement and tomography reconstruction.
Beam profiles hint that the beam is close to Gaussian.
105

## Slide 106: Reconstruction of the RFQ output beam
Tomography reconstructed data indicates:
actual RFQ output beam is close to Gaussian and to the beam dynamics simulation.
Tomography:
ex= 0.0964
ey= 0.0782
106

## Slide 107: MEBT beam size fitting
MEBT
SCL
X beam size
Y beam size
Beam size fitting method
using Gaussian initial beams
ex= 0.0894 mm-mrad
ey= 0.0606 mm-mrad
107

## Slide 108: Tomography vs Beam size fitting
Excellent agreement is observed between the tomography method and the beam size fitting method, primarily because
the actual RFQ output beam is close to Gaussian;
Beam size fitting method uses Gaussian input beams.
Tomography emittances are slightly bigger due to the low intensity tails.
 | Tomography | Beam size fitting
ex (rms, mm-mrad) | 0.0964 | 0.0894
bx (mm/mrad) | 0.833 | 0.758
ax | -2.726 | -1.907
ey (rms, mm-mrad) | 0.0782 | 0.0606
by (mm/mrad) | 1.194 | 1.141
ay | 3.182 | 3.588
108

## Slide 109: Tomography in the LEBT
Tomography reconstruction was applied using the 4 wire-scanners in the LEBT.
There are two dipoles in the LEBT and the beam energy is 10 keV/u.
Nonlinear effects can be important.
In the LEBT, there are Allison emittance scanners.
Excellent opportunity to validate the tomography reconstruction with the actual emittance data.
109

## Slide 110: How to handle nonlinearities
It should be noted that there are two dipoles in the LEBT.
The beam energy is only 10 keV/u even though the beam current is 50 uA.
It may be necessary to include the space charge effect and the 2nd order geometric and magnetic field effects of dipoles.
110

## Slide 111: Measurement vs. Tomography (LEBT wire-scanners) with space charge & 2nd order
Beam is far from Gaussian in the LEBT.
Tomography reconstruction manifests good agreement between the measurement and tomography reconstruction.
Quality of Y reconstruction is inferior to X.
111

## Slide 112: Comparison with the Allison data with space charge & 2nd order
Tomography
ex= 0.0534 mm-mrad
ey= 0.0655 mm-mrad
Allison
ex= 0.0668 mm-mrad
ey= 0.0584 mm-mrad
Excellent reconstruction.
Data quality in Y plane is inferior.
112

## Slide 113: LEBT beam size fitting
Beam size fitting method
using Gaussian initial beams
ex= 0.0412 mm-mrad, bx= 2.073, ax= 0.012
ey= 0.0384 mm-mrad, by= 2.874, ay= 0.497
LEBT
RFQ
113

## Slide 114: Comparison
Comparison of emittance data vs tomography vs beam size fitting.
Tomography method reconstructs the beam distribution well even when the actual beam is far from Gaussian.
Beam size fitting method is not accurate, for the actual LEBT beam is far from Gaussian (pronounced tails and deformation).
 | Allison scanner | Tomography | Beam size fitting
ex (rms, mm-mrad) | 0.0668 | 0.0522 | 0.0412
bx (mm/mrad) | 2.197 | 2.782 | 4.771
ax | 0.312 | 0.198 | 0.105
ey (rms, mm-mrad) | 0.0584 | 0.0616 | 0.0384
by (mm/mrad) | 2.188 | 3.327 | 4.438
ay | -0.198 | -0.834 | -0.289
114

## Slide 115: Comparison with the Allison data with and without nonlinear effects
with nonlinear effects
without nonlinear effects
Allison data

## Slide 116: Space charge effects: particle resonances & parametric instabilities why zero current phase advance is limited below 90° for high intensity linear accelerators

## Slide 117: Physics of high intensity beam
Beam self-field effect is called “space charge effect”.
Space charge field can be comparable to the external focusing field for today’s accelerators.
Space charge potential has many nonlinear terms that can drive interesting nonlinear effects.
Accelerator is a rich source of nonlinear dynamics.
external potential
potential by space charge effect
beam

## Slide 118: Resonances in circular accelerators
has been known for a long time for circular accelerators.
happens when beam passes through the same point (kick) over and over.
widely known that there is no resonance in linear accelerators …
accelerator
beam
kick

## Slide 119: 4n=1 resonance in circular accelerators
4 stands for the order of the potential term ~ X4 of Hamiltonian.
1/4 stands for the tune (= 90°/360°).
There are four stable and unstable fixed points.
stable fixed points
unstable fixed points

## Slide 120: Drowned in a swamp of terms…?
Resonances
Incoherent
resonances
Instabilities
Coherent
resonances
Coherent
instabilities
Parametric
instabilities
Parametric resonances
Structure
resonances

## Slide 121: Space-charge halo mechanisms
There are largely two families of space-charge mechanisms: particle resonances and parametric instabilities.
Their differences were well pointed out in references:
(particle) resonances: a.k.a. single particle resonances, resonances, incoherent resonances …
(parametric) instabilities: a.k.a. parametric resonances, structure resonances, coherent resonances, coherent instabilities, mode instabilities, instabilities …
Here, we focus on space charge mechanisms in linear accelerators.
Jeon et al, NIM A 832, 43 (2016);
Jeon, J Korean Phys Soc 72, 1523 (2018)
121

## Slide 122: There are look-alike people
There are look-alike people ...
But they have different parents.

## Slide 123: What is the difference?
(parametric) instabilities
(particle) resonances
FFT resonance frequency component O
FFT resonance frequency component X
Parametric instabilities : Fixed points do not exist in the phase space.
Particle resonances : Fixed points exist in the phase space.

## Slide 124: Parametric Instability vs Particle Resonance
parametric instability
particle resonance
KV distribution
so=112
s=85~93
Gaussian dist.
Jeon, J Korean Phys Soc 72, 1523 (2018)
FFT resonance frequency for the particle resonance.
No FFT resonance frequency for the parametric instability.

## Slide 125: Particle resonances in linear accelerators

## Slide 126: Particle resonances in high-intensity linacs
(Particle) Resonances in circular accelerators are well known.
In 2009, 4s = 360 particle resonance was discovered in high-intensity linacs. [Jeon et al, PRST-AB 12, 054204 (2009)]
Confirmed by two experiments.
In 2015, 6s = 720 particle resonance was discovered. [Jeon et al, PRL 114, 184802 (2015)]
In 2016, higher order particle resonances were discovered:
8s = 1080 resonance, 10s = 1440 resonance [Hofmann, HB2016]
126

## Slide 127: 4th order particle resonance in high-intensity linacs
FFT frequency spectrum
Jeon et al, PRST-AB 12, 054204 (2009)
4s = 360 particle resonance in high-intensity linacs discovered in simulations.
Resonance effect in 90° < so and s < 90.
FFT resonance frequency peak at 1/4.
Confirmed by two experiments.
1/4
s=85°
s=75°
s=92°
tune
127

## Slide 128: Experiment 1: 4th order particle resonance GSI UNILAC
simulation
X
Px
Groening et al, PRL 102, 234801 (2009)
so [deg]
128

## Slide 129: Experiment 2: 4th order particle resonance SNS linac
simulation
experiment
Jeon, PRAB 19, 010101 (2016)
simulation
experiment
s=80°
s=88°
s=65°
s=80°
s=65°
s=80°
s=80°
s=88°

## Slide 130: 6th order particle resonance in high-intensity linacs
FFT analysis shows a peak at 1/3.
6s = 720 particle resonance in s < 120.
No resonance effects in s > 120.
6th order resonance
Jeon et al, PRL 114, 184802 (2015)
Gaussian dist.
1/3

## Slide 131: 6th order particle resonance in high intensity linear accelerators
Resonance frequency peak at 1/3 for lattice s < 120 for non-KV beams.
No resonance effect for s > 120.
6th order resonance
10 mA Gaussian beam
6th order resonance
20 mA waterbag beam
Jeon, J Korean Phys Soc 72, 1523 (2018)
Gaussian dist.
waterbag dist.

## Slide 132: Parametric instabilities

## Slide 133: Parametric instabilities
x
y
Examples of eigenmodes of Vlasov-Poisson model
(Parametric) instabilities are instabilities of beam eigenmodes.
Beam eigenmodes of Vlasov and Poisson equations.
Analytical solution is available only for the KV distribution.
Beam
distribution
Courtesy of Hofmann, PRE 57, 4713 (1998)

## Slide 134: Parametric instabilities
In 1959, Kapchinskij and Vladimirskij found a self-consistent high-intensity beam distribution (called “KV distribution”) and derived the envelope equation: .
In 1979, Haber et al. found an instability of KV distribution.
In 1983, Hofmann derived various instabilities of KV distributions from Vlasov-Poisson equations:
instabilities of beam eigen-modes.
The 2nd order instability is widely called “the envelope instability”.
They are also called “parametric resonances” by some.
They are not resonances of beam particles.
Moreover, there are also parametric resonances of “particles”, which causes confusion.
Haber et al, PRL 42, 1479 (1979)

## Slide 135: envelope instability (2nd order) in high intensity linear accelerators
Envelope instability for a constant- so lattice with so = 100 and s = 70.
Observed for KV, Gaussian, waterbag distributions in so > 90°.
The envelope instability is excited following the 4th order resonance.
Gaussian distribution

## Slide 136: When does the envelope instability develop?
The envelope instability manifests when the 4th order resonance fades away (as s goes near and above 90) for non-KV beams.
Jeon et al, NIM A 832, 43 (2016)
Gaussian dist.
so = 100° linac
136

## Slide 137: 3rd order instability in high intensity linear accelerators
3so –Ds3,coh = 180 instability for a lattice with so = 92 and s = 40 (90 mA beam).
Observed for KV and waterbag distributions, but not for Gaussian distribution.
Not a particle resonance: no resonance peak around 1/3 or 1/6 in the FFT spectrum.
waterbag distribution
Jeon et al., NIM A 832 (2016) 43
1/6
1/3

## Slide 138: 4th order instability in high intensity linear accelerators
4so –Ds4,coh = 360 instability for a lattice with so = 112 and s = 85.
Observed only for a KV distribution when s is close to 90°.
Not a particle resonance: no resonance peak around 1/4 in the FFT spectrum.
KV distribution
Jeon, J Korean Phys Soc 72, 1523 (2018)
1/4

## Slide 139: 4th order instability in high intensity linear accelerators
These are 4so –Ds4,coh = 180 instability.
Observed mainly for KV and waterbag distributions.
Observed when s is far away from 90°.
Courtesy of Hofmann (HB2016)
waterbag distribution
so = 70 and s = 35
Courtesy of Haber and Maschke,
PRL 42, 1479 (1979)
KV distribution
so = 90 and s = 30

## Slide 140: Parametric instabilities observed in multiparticle simulations
s=90°
s=120°
3(so-Dscoh)
=180º
instability
waterbag
4(so-Dscoh)
=180º
instability
KV
s=30°
4(so-Dscoh)
=360º
instability
KV
envelope
instability
non-KV, KV
4(so-Dscoh)
=180º
instability
waterbag
s=60°
s=135°
3rd and 4th order parametric instabilities have been observed in multi-particle simulations for waterbag distribution and KV distribution.
140
s : depressed phase advance per period
so : zero current phase advance

## Slide 141: Parametric instabilities in actual linacs?
Few parametric instabilities have been observed in multiparticle simulations for waterbag distribution;
But, not observed for Gaussian distribution,  indicating that most of parametric instabilities are not observable in actual linacs.
Parametric instability | KV | waterbag | Gaussian
2nd order | Observed | Observed | Observed
3rd order, 4th order | Observed | Observed | Not observed
higher order | Observed | Not observed | Not observed
- Jeon, J. Korean Phys. Soc. 72, 1523 (2018);
HB2018 and Space Charge 2019
141

## Slide 142: No 3rd order parametric instability in actual linacs
waterbag dist
so=92°, s=40°, 80 mA
Gaussian dist
realistic dist
3rd order parametric instability is not manifested for Gaussian or realistic distributions.
Jeon et al, Nucl Eng. Technol. 58, 104379 (2026)

## Slide 143: No 4th order parametric instability in actual linacs
waterbag dist
Gaussian dist
realistic dist
so=71°, s=35°, 40 mA
4th order parametric instability is not manifested for Gaussian or realistic distributions.
Jeon et al, Nucl Eng. Technol. 58, 104379 (2026)

## Slide 144: Landau damping
Landau damping suppresses most of parametric instabilities except the envelope instability for Gaussian distribution.
Only the envelope instability is observable in actual linacs.
Hofmann et al, PRAB 24, 024201 (2021)
Waterbag distribution
Gaussian distribution
144

## Slide 145: Envelope instability effect reduced for (SNS) realistic distribution
Realistic distribution of SNS 35-mA H- beam is used.
4th order particle resonance effect is stronger for realistic distribution.
However, onset of the envelope instability is delayed, emittance growth reduced.
Jeon et al, Nucl Eng. Technol. 58, 104379 (2026)

## Slide 146: Envelope instability effect reduced for (SNS) realistic distribution
For a lattice with flat so ≈ 100°, s stays below 90° and envelope instability not induced.
Mismatch (by increasing bx and by by 20%) increases beam emittance.
Jeon et al, Nucl Eng. Technol. 58, 104379 (2026)

## Slide 147: Related Experiments

## Slide 148: No sign of parametric instabilities in experiment data
Tiefenback’s thesis stated: Our work shows no evidence of any unstable behavior … up to about so = 88°.
No sign of parametric instabilities in the GSI experiment:
Tiefenback’s thesis, LBL Report No LBL-22465 (1986)
Groening et al, PRST-AB 11, 094201 (2008)
2strans - 2slong = 0 resonance
so [deg]
Trans. emittance [mm mrad]
4s = 360° resonance
so [deg]
Trans. emittance [mm mrad]
Groening et al, PRL 102, 234801 (2009)
148

## Slide 149: Tiefenback’s experiment
Tiefenback’s PhD thesis (1986) reported an experiment observation of “four-pointed structure” for the so=98° lattice.
But misidentified it as the “fourth order structure resonance” (parametric instability).
It was the fourth-order particle resonance.
Figure 5.15 of Tiefenback’s thesis
so=98° lattice
149

## Slide 150: In multi-particle simulations
Around particle resonances, no parametric instabilities are manifested except the envelope instability for non-KV beams.
The rest parametric instabilities manifest away from particle resonances for waterbag beam, but not for Gaussian.
s=90°
s=120°
3(so-Dscoh)
=180º
instability
waterbag
4th order
resonance
non-KV
6th order
resonance
non-KV
4(so-Dscoh)
=180º
instability
KV
s=30°
4(so-Dscoh)
=360º
instability
KV
envelope
instability
non-KV, KV
8th, 10th order
resonance
non-KV
4(so-Dscoh)
=180º
instability
waterbag
s=60°
s=135°
150

## Slide 151: However, in actual linear accelerators
s=90°
s=120°
4th order
resonance
non-KV
6th order
resonance
non-KV
s=30°
8th, 10th order
resonance
non-KV
s=60°
s=135°
Only particle resonances and the envelope instability are observable in actual linacs.
The rest parametric instabilities are damped by Landau damping.
envelope
instability
non-KV
151

## Slide 152: Summary
Particle resonances and the envelope instability are observable in actual high-intensity linear accelerators.
The rest parametric instabilities are damped by Landau damping in actual linear accelerators.
Realistic distributions show that onset of the envelope instability is delayed and the emittance growth reduced.
152

## Slide 153: ECR Ion Source Design
ECR field surface
Axial field
Radial field
3D modeling
Boundary condition :
Design result :
Binj= 3.61 T, Bext= 2.07 T, Br= 2.17 Becr , Bmin= 0.545 T
Binj >3.5Becr , Bext~2Becr , Br~2Becr , Bmin~0.8Becr