## Slide 1: Fabrication Technology of QCS magnets for Super-KEKB
Asian School on Superconductivity and Cryogenics for Accelerators
February 13-19, 2023
TAEHYUN KIM

## Slide 2: Contents
0
What is MITSUBISHI ELECTRIC?
Superconducting magnets and coils
3-1. Introduction of QCS magnets for Super-KEKB
3-2. Fabrication of QCS magnets
3-3. Accurate assembly of cryostat
3-4. High voltage testing
4. Wiring
5. QCSR in factory
6. Conclusion

## Slide 3: What is MITSUBISHI ELECTRIC?
1
What is MITSUBISHI ELECTRIC?
3
Nagasaki
Electrical Motor
Plant Engineering
Generator (Thermal, Hydro, Nuclear)
Instrument & Control System
Electrical grid control & monitoring system
Accelerator/Superconductor application
Power information & communication system
Yokohama
Kobe
ESC
Energy Systems Center(ESC)
Energy (thermal)
Accelerator/ Superconductor application systems
Energy (hydroelectric)
Energy (nuclear)
Power system solution
Sales ratio by business field
KOBE

## Slide 4: Superconducting magnets and coils
2
・Mitsubishi Electric manufactures SC-magnets and SC-coils from 1980’s
For example,
SC-Combined Function magnets for Neutrino Beam Line at J-PARC
Final Focus SC-magnets, QCS-R/L, for SuperKEKB
Pion Capture Solenoid for COMET (just going)
Poloidal Field SC-coils, EF and CS, for JT-60SA
Winding Pack of Toroidal Field coils for ITER
・Mitsubishi Electric have developed Continuous automatic winding cable-in-conduit conductor (CICC) techniques
If you interest, check the following.
“https://www.giho.mitsubishielectric.co.jp/giho/pdf/2019/1911113.pdf”
It is used to manufacture large scale SC magnets for experimental fusion reactor.
First Winding Pack of TF coil for ITER in JAPAN
Source: Abstracts of CSSJ conference Vol.97 P125

## Slide 5: Introduction of QCS magnets for Super-KEKB
3-1
QCS is final focus system of SuperKEKB
（Target luminosity is 40 times as KEKB）
Squeezing to extremely small beam at interaction point
（1/20 as KEKB，10μm×0.05μm）
⇒Many superconducting magnets are installed in cryostats for beam focusing.
（Requirement of accurate winding and assembly）
QCS-R
QCS-L
Interaction Point
Belle-Ⅱ Particle Detector

## Slide 6: Introduction of QCS magnets for Super-KEKB
3-1
Horizontally flipped previous photo

## Slide 7: Introduction of QCS magnets for Super-KEKB
Superconducting solenoid magnets for compensating of Belle Ⅱ detector field
Superconducting quadrupole magnets for beam focusing
3-1
Layout of magnets
Positron（4GeV）
Electron（7GeV）
Horizontally flipped previous photo

## Slide 8: Introduction of QCS magnets for Super-KEKB
3-1
Front region of QCS-R
Electron
（7GeV）
Positron（4GeV）

## Slide 9: Introduction of QCS magnets for Super-KEKB
3-1
QCS-R
QCS-L
Magnet cryostats
3287 mm
2724 mm
 | QCS-R | QCS-L
Quadrupole magnets | 4 | 4
Solenoid magnets | 3 | 1
Corrector magnets | 23 | 20
Superconducting magnets in Magnet cryostats
Fabrication at MELCO
Assembly of magnet and service cryostats in MELCO
Service cryostat
Including
30 magnets
Including
25 magnets

## Slide 10: Fabrication of QCS magnets
3-2
Electron
（7GeV）
Positron（4GeV）
Quadrupole magnet
Solenoid magnet
Beam line with quadrupole of QCS-R

## Slide 11: Fabrication of QCS magnets
3-2
Electron
（7GeV）
Positron（4GeV）
Quadrupole magnet

## Slide 12: Fabrication of quadrupole magnet
3-2
 | QC1LP | QC1RP | QC1LE | QC1RE
Design （mm) | 384 |  | 430 | 
Average length（mm） | 384.00 | 383.98 | 429.98 | 429.92
1 σ | 0.044 | 0.006 | 0.041 | 0.010
Design （mm) | 5.425 |  |  | 
Average thickness（mm） | 5.418 | 5.423 | 5.425 | 5.418
1 σ | 0.006 | 0.002 | 0.003 | 0.002
Cross section
of QC1P
Cable winding
Coil length and thickness measured after curing
Rutherford type NbTi cable
Width 2.5 x Thickness 0.93 mm
Accurate fabrication

## Slide 13: Fabrication of quadrupole magnet
3-2

## Slide 14: Assembly of beam line with quadrupole
3-2
Beam line with quadrupole of QCS-R
Electron
（7GeV）
Positron（4GeV）

## Slide 15: Fabrication of quadrupole magnet
3-2
Key of compensating
magnet
Key of quadrupole
magnet
Key of compensating
magnet
Key of quadrupole
magnet
Quadrupole
magnetic field

## Slide 16: Fabrication of solenoid magnet
3-2
Electron
（7GeV）
Positron（4GeV）
Solenoid magnet

## Slide 17: Fabrication of solenoid magnet
3-2
Solenoid is placed in narrow space between outer Belle II, and, inner beam line magnets
1575 mm
Constraints:
For outer shape, Belle Ⅱ bore, and radiation shield.
For Inner shape, beam line magnets.
For magnetic field, Belle Ⅱ solenoid field compensation.
IP side

## Slide 18: Fabrication of solenoid magnet
3-2
IP side
Winding frame（White area，minimum thickness of 5mm）
Winding（Red area, total 6237 turns, 15 divisions）
1575 mm
Constraints lead to very thin structure, and divided windings.
Design minimum gap of 2mm between winding and radiation shield.
Assembly was completed successfully.
Radiation shield

## Slide 19: Fabrication of solenoid magnet
3-2

## Slide 20: Accurate assembly of cryostat
3-3
Electron
（7GeV）
Positron（4GeV）
Front region of cryostat

## Slide 21: Accurate assembly of cryostat
3-3
He vessel
Vacuum vessel
Rod
Alignment of magnets
Tolerance of± 0.2 mm from beam axis at room temperature
Different configuration of inner and outer area of He vessel leads to different approach of alignment.
→ Inner area of He vessel: No constraint for heat transfer by liquid He filling.
Use alignment key provided by machining
Densely packed components
Vacuum
Liquid He filling

## Slide 22: Accurate assembly of cryostat
3-3
He vessel
Vacuum vessel
Rod
Alignment of magnets
Tolerance of± 0.2 mm from beam axis at room temperature
Different configuration of inner and outer area of He vessel leads to different approach of alignment.
→ Outer area of He vessel: Preventing heat transfer, vacuum insulation.
Using rod
Influence of thermal expansion coefficient, electromagnetic force.
EM force of 36 kN act on Solenoid compensating Belle Ⅱ field.
Vacuum
Liquid He filling

## Slide 23: Alignment structure inner side of He vessel
3-3
Magnet fixing support was manufactured
Holding of quadrupole magnets
Two beam lines
Tolerance: Displacement of ± 0.1 mm Rotating angle of ± 2 mrad
83mrad

## Slide 24: Alignment structure inner side of He vessel
3-3
QC2RP，4 corrector
Corrector, magnetic shield yoke
Corrector, magnetic shield yoke
QC1RE，4 corrector
QC1RP，5 corrector
4 leak field cancel magnet
Quadrupole magnets on the support

## Slide 25: Alignment structure inner side of He vessel
3-3
magnet
Support
High precision machining provided the accurate alignment surfaces on the support.
⇒Displacement error of less than 0.2 mm between axis of magnet and beam line
Alignment structure for quadrupole magnets
Alignment
key
Alignment
key
Axis of magnet
Alignment
surface
Alignment
surface

## Slide 26: Alignment structure inner side of He vessel
3-3
Support
High precision machining provided the accurate alignment surfaces on the support.
⇒Displacement error of less than 0.2 mm between axis of magnet and beam line
Alignment
surface
Alignment
surface

## Slide 27: Alignment structure outer side of He vessel
3-3
He vessel must be aligned to vacuum vessel of cryostat accurately. ・Supported from Eight rods
・Accurate alignment mark on vacuum vessel
He vessel
Vacuum vessel
Rod
Requirement for alignment
Preload is applied to rods, in order to withstand EM force to He vessel induced by operation.
Vacuum
vessel
He vessel

## Slide 28: Alignment structure outer side of He vessel
3-3
Laser tracker
Axis of vacuum vessel
Reflector
Vacuum vessel
Vacuum vessel
Alignment hole
of vacuum vessel
Alignment mechanism
He vessel
Rod
Alignment hole
of vacuum vessel
Alignment mechanism
Axis of vacuum vessel was evaluated with Laser tracker using alignment holes
Alignment hole
of He vessel

## Slide 29: Alignment structure outer side of He vessel
3-3
Vacuum vessel
Alignment hole
of vacuum vessel
Alignment mechanism
He vessel
Rod
Alignment hole
of He vessel
Source: AFAD2018

## Slide 30: Alignment structure outer side of He vessel
3-3
Vacuum vessel
Alignment hole
of vacuum vessel
Alignment mechanism
He vessel
Rod
Alignment hole
of He vessel

## Slide 31: Alignment structure outer side of He vessel
Vacuum vessel
Alignment hole
of vacuum vessel
Alignment mechanism
He vessel
Rod
Alignment hole
of He vessel
3-3
He vessel was aligned to axis of vacuum vessel.
・Alignment holes of He vessel were used as measurement reference.
・Alignment holes were measured with laser tracker.
・Position of alignment holes were adjusted with alignment mechanism
⇒ Coaxiality less than 0.2 mm, which is target position displacement, were achieved for two beam line at room temperature.
Preload requirements of rods were satisfied.
⇒Assembly for front region of QCS-R cryostat was completed.

## Slide 32: High voltage testing
3-4
One of requirement of High voltage testing is He ambient.
Withstand voltage of He gas is as 1/10 times or less as Air.
Gap filled with gas He is easy to breakdown.
Therefore, insulation of winding is important.
The results is acceptable
Winding（Red area）
Radiation shield

## Slide 33: Wiring
4

## Slide 34: QCSR in factory
5

## Slide 35: Conclusion
6
・Fabrication of QCS-R and QCS-L were completed.
・QCS-R and QCS-L provided steady operating in SuperKEKB
We would like to show our deep appreciation to KEK members for continuously supporting to fabrication.
QCS-R
QCS-L