## Slide 1
2023. 2. 16
QWR and HWR Cryomodules for Heavy Ion Accelerator in RAON/RISP
Heavy-Ion Accelerator Research Institute, IBS
Youngkwon Kim

## Slide 2
Contents
Introduction
  Overview
  RAON layout
  Project milestone
  Introduction of SCL3
Introduction on cryomodule
Design issue of cryomdoule
Mass production of SCL3 cryomodules
Installation and commissioning
1
2
3
4
5

## Slide 3
Providing high intensity RI beams by ISOL and IF
ISOL: direct fission of 238U by 70 MeV proton
IF: 200 MeV/u 238U (intensity: 8.3 pμA)
Providing high quality neutron-rich beams
e.g., 132Sn with up to 250 MeV/u,
up to 109 particles per second
Providing More exotic RI beam
production by combination of ISOL and IF
Budget: KRW 1,432 billion (US$ 1.26 billion, 1$=1,135krw)
- accelerators and experimental apparatus : 460.2 billion won
- civil engineering & conventional facilities : 972 billion won (incl. site 357 billion won)
Period: 2011.12 ~ 2021.12
Goal: To build a heavy ion accelerator complex RAON,
for rare isotope science research in Korea.
* RAON - Rare isotope Accelerator complex for ON-line experiments
Construction of research and support facility to ensure the stable operation of the heavy-ion accelerator, experiment systems, and to establish a comfortable research environment
※ Accelerator and experiment buildings, support facility, administrative buildings, and guest house, etc.
Development, installation, and commissioning of the accelerator systems that provides high-energy (200MeV/u) and high-power (400kW) heavy-ion beam
System Installation Project
Facility Construction Project
Overview

## Slide 4
RAON layout
IF System
BIS
μSR
HPMMS/
CLS
SCL2
ISOL System
LAMPS
Cyclotron
SCL3
SCL1
ECR IS
KOBRA
NDPS
Control
Center
Utility
HRS
SCL1 has been decided to be postponed
: SCL3 is going to be taking a role of SCL1 in the early operation

## Slide 5
Project milestone
Project milestone of RAON were modified 3 times as in 2015, 2018, and 2021 due to;
  Too optimistic and aggressive plan at planning phase of RAON
  RAON project launched with absolutely nothing prepared for the project: no people, no facility, no technology
  A lot of trial & errors from lacks of technology and experience during implementation
Current status
  To separate installation of low energy linac(SCL3) and high energy linac(SCL2) as phase 1 and phase 2, respectively
  Beam commissioning of SCL3 is on-going and planned to finish in April 2023.
  The 1st step of phase 2, R&D of SCL2 cryomdoules will go during coming 3 years, 2023~2025

## Slide 6: Introduction on SCL3
RF Parameter of QWR and HWR
 | QWR | HWR
βopt | 0.047 | 0.12
f [MHz] | 81.25 | 162.5
Leff | 173.5 | 221.5
R/Q [Ω] | 469 | 295
Ep/Eacc | 5.7 | 5.2
Bp/Eacc [mT/(MV/m)2] | 10.4 | 9
Eacc [MV/m] | 6.1 | 6.6
Vacc [MV] | 1.06 | 1.46
QRs | 18.1 | 36.8
Layout of RAON
 | Cavity | # of cav. | # of CM | Cav. Op. T (K)
SCL1,3 | QWR | 1 | 22 | 4.5
 | HWR | 2 | 13+2 | 2.05
 |  | 4 | 19 | 2.05
SCL2 | SSR1 | 3 | 23 | 2.05
 | SSR2 | 6 | 23+2 | 2.05

## Slide 7
Contents
Introduction
Introduction on cryomodule
  Role of cryomodule
  Requirements for RAON cryomodule
  Configuration of RAON cryomdoule
Design issue of cryomdoule
Mass production of SCL3 cryomodules
Installation and commissioning
1
2
3
4
5

## Slide 8: Role of cryomodule
Integration of cavities, power couplers, tuners, cryogenic pipelines, etc.
Cryomodule maintains operating condition of superconducting cavities
  Thermal insulation for cryogenic operation
  Vacuum insulation
  Shielding of earth’s magnetic field (500 mG  ~10 mG)
  Alignment of cavity
Interface between the components of accelerators and utilities
  Warm section (vacuum chamber, quadruple magnets, beam pipes, etc.)
  Valve box of CDS (cryogenic distribution system)
  Pressurized air for actuator(cryogenic valve, gate valves, etc.) or cooling system(inner conductor, etc.)
  Signal lines (temperature and pressure sensors, valves, actuators, etc.)
  RF transmission lines, and so on…

## Slide 9: Requirements for RAON Cryomodules
 |  | QWR | HWR CMA | HWR CMB
Size | Width | Less than 1.6 m |  | 
 | Length, mm | 610 | 1130 | 2010
 | Height | Less than 3.5 m |  | 
Operating Temp. | THS | 40 K |  | 
 | Pipe lines | 4.5 K or 2.05 K |  | 
 | Cavity | 4.5 K | 2.05 K | 
Alignment | x, y | ± 1 mm |  | 
 | z (beam direction) | ± 1 mm |  | 
 | tilt | ± 0.28 ° |  | 
Pressure ratings | Helium jacket / reservoir | Room temp.: 2 bar(a) internal Cold temp.: 4 bar(a) internal |  | 
 | THS cooling line | 20 bar(a) internal |  | 
 | Vacuum vessel | 1 bar (a) external |  | 
Magnetic shield |  | 15 mG |  | 
Vacuum | Cavity | Less than 10-9 mbar at cold |  | 
 | Vacuum vessel | Less than 10-5 mbar at cold |  | 

## Slide 10: Configuration of RAON SCL3 Cryomodule
Cryomodule assembly
Magnetic shield
(mu-metal)
Thermal shield
(Al plate + Cu pipe)
View port for open target

## Slide 11
Beamline gate valve
Cryogenic valve
Pressure safety system
(rupture disk, relief valve, solenoid valve)
Tuner
Power coupler
4 K reservoir
2 K reservoir
Cavity vacuum manifold
Helium guard for 2 K pressure safety
Rupture disk for helium guard
Cryogenic pipe lines to valve box
All-metal angle valves
Strong-back

## Slide 12
Inner conductor
Thermal intercept
Outer conductor
Cryogenic motor
Contact with cavity beam port flange
Power coupler
Tuner

## Slide 13
Contents
Introduction
Introduction on cryomodule
Design issue of cryomdoule
  Thermal design
  Sizing for HeII heat transfer
  Alignment of cavity
Mass production of SCL3 cryomodules
Installation and commissioning
1
2
3
4
5

## Slide 14: Thermal design
Thermal design
Minimizing heat ingress from the ambient
Estimation of thermal load at each temperature level (2 K, 4.5 K, 40 K , etc.)
 Determine the size of cryogenic system
Convection
  No convection in cryomodule by vacuum pumping below 10-5 mbar
Conduction
  Reducing cross-sectional area and increasing heat transfer path
  Thermal intercepts connected with intermediate temperature (40 K and 4.5 K)
Radiation
  Thermal shield cooled by GHe (tunnel) or LN2 (test facility)
  Multilayer insulation (MLI)

## Slide 15: Thermal design
Radiation heat load
Using material with shine surface(small ε) or MLI(multilayer insulation)
Reducing temperature difference
 – Boltzmann constant = 5.67 *10-8 W/m2
A – emitter area
ε – emissivity

## Slide 16: Thermal design
Thermal shield: reducing the temperature difference
Using material with shine surface(small ε) or MLI(multilayer insulation)
Reducing temperature difference

## Slide 17: Thermal design
MLI: reducing effective emissivity
Using material with shine surface(small ε) or MLI(multilayer insulation)
Reducing temperature difference

## Slide 18: Thermal design
LHe
LN2
Vacuum Jacket
MLI
MLI: reducing effective emissivity
Analytical calculation!!!
 How many layers? Actual heat ingress through MLI??

## Slide 19: Thermal design
Actual heat flux with THS and MLI
Worst case scenario calculation [1]
  10-4 Torr, e=0.2, keff=0.15 W/m-K: 2.5 W/m2 at 50 K (four 15 layers MLI)
  10-4 Torr, e=0.06, keff=0.15 W/m-K: 0.094 W/m2 (two 12 layers MLI)
Experiment with LHC magnet [2]
  0.8 W/m2 at 50 K (30 layers MLI)
  0.05 W/m2 at 1.9K (10 layers MLI)
[1] E.F. Daly et al., Spallation neutron source cryomodule heat loads and thermal design, Adv. Cryog. Eng, vol. 47A, p531-539
[2] L. Dufay et al., A large-scale test facility for heat load measurements down to 1.9 K, CEC/ICMC2001, p16-20, July 2011, Madison, Wisconsin, USA

## Slide 20: Thermal design
Actual heat flux with THS and MLI
Empirical formula [3]
Experiment with ILC cryomodule in KEK [4]
  1.51 W/m2 at 80 K (30 layers MLI)
  0.041 W/m2 at 5K (10 layers MLI)
[3] T.C. Nast et al., Multilayer insulation considerations for large propellant tanks, Cryogenics, 64, p105-111, 2014
[4] N. Ohuchi et al., Study of thermal radiation shields for ILC cryomdule, Adv. Cryog. Eng., p929-936, 2012

## Slide 21: Thermal design
Actual heat flux with THS and MLI
Thermal load through MLI for RAON cryomodule thermal load estimation
  300 K to 40 K with 30 layers of MLI: 1.5 W/m2
  40 K to 2 K with 10 layers of MLI: 0.05 W/m2

## Slide 22: Thermal design
Conduction heat load
Using low conductivity materials such as GFRP, STS, etc.
Reducing cross-sectional area
Increasing heat transfer path
  P. Duthil, Material properties at low temperature

## Slide 23: Thermal design
Bellows: reducing area and increasing length
Support post
  T. Nicol, “Design and analysis of the SSC dipole magnet suspension system.”, 1989, IISC
Warm-to-cold transition beam pipe
Conduction heat load

## Slide 24: Thermal design
Thermal intercepts
4 K
300 K
Cross-sectional area: A
Thermal conductivity: k
Length: L
x
T (K)
L

## Slide 25
Thermal intercepts
4 K
300 K
Cross-sectional area: A
Thermal conductivity: k
Length: L
x
T (K)
x1
L-L1
L1
Thermally connected with
thermal shield
Reduced 4 K thermal load but NEW 40 K thermal load !!!!
 How to determine the intercept position??

## Slide 26
Thermal intercepts
How to determine the intercept position? or How to optimize the thermal load ?
Coefficient of Performance:
: Work required for 1 W cooling at low temperature (TL)
 | Ref. 1 |  | Ref. 2 |  | Ref. 3
 | COP-1 | COP ratio | COP-1 | COP ratio | COP ratio
2 K | 800 | 3.2 | 714 | 3.66 | 3
4.5 K | 250 | 1 | 200 | 1 | 1
40 K | 25 | 0.1 |  |  | 0.1
77 K | 14 | 0.056 | 16 | 0.08 | 
C. Pagani et al., Cryomodule design, assembly and alignment, SRF 2003
E. Chojnacki et al., Cryogenic heat load of the Cornel ERL main cryomodules, SRF 2009
F. Casagrande et al., Integrated thermal analysis of the FRIB cryomodule design, IPAC2012
COP ratio = (COP-1at T) / (COP-14.5K)
Position minimizing equivalent thermal load!
Ref.
TH
TL
W
QL
QH

## Slide 27
J. W. Ekin, Experimental techniques for low temperature measurements
Chart: x
| 0.1 | 0.15 | 0.2 | 0.25 | 0.3 | 0.35 | 0.4 | 0.45 | 0.5 | 0.55000000000000004 | 0.6 | 0.65 | 0.7 | 0.75 | 0.8 | 0.85 | 0.9 | 0.95
 | 1.1548 | 0.89964 | 0.7842 | 0.72661 | 0.70004 | 0.69352 | 0.70227 | 0.72449 | 0.76032 | 0.81151 | 0.88173 | 0.97751 | 1.1102 | 1.3009 | 1.5918 | 2.082 | 3.0692 | 6.0419
4 K
Simple example

## Slide 28
https://trc.nist.gov/cryogenics/materials/materialproperties.htm
NIST cryogenic material properties

## Slide 29
Margin of thermal load estimation
Qtotal = F0 X (Qd X Fd + Qs X Fs)
  F0: Redundancy and degradation HRS (1.15)
  Fd: beam loss, uncertainty of dynamic load (1.3 ~ 1.1)
  Fs: Uncertainty of static load (1.3~1.1)
50 % margin for estimated thermal load
Heat load |  | QWR (22 EA) |  |  | HWR CMA (13+1 EA) |  |  | HWR CMB (19 EA) |  | 
 |  | 2.05 K | 4.5 K | 35 – 55 K | 2.05 K | 4.5 K | 35 – 55 K | 2.05 K | 4.5 K | 35 – 55 K
Estimated without margin | Static | - | 5.0 | 55.5 | 3.0 | 3.0 | 78.6 | 4.5 | 5.0 | 121.0
Estimated with 50% margin | Static | - | 7.5 | 83.3 | 4.5 | 4.5 | 117.9 | 6.8 | 7.5 | 181.5
Measured in tunnel (average)* | Static | - | 4.5 |  | 4.3 | 5.1 |  | 6.1 | 6.8 | 
Estimated and measured static thermal load for cryomodules
*: measurement result shown in later slide for static thermal load

## Slide 30: Sizing for HeII heat transfer
He II heat transfer
Thermal conductivity function at 2.05K: 6500 kW3/m5〮K
Depth of HeII in helium jacket: ~1 m
Peak heat flux:
Peak heat flux=0.969 W/cm2 ∼1W/cm2
V. Sciver, Helium cryogenics 2nd ed.
T. Peterson, Notes about the limits of heat transport from a TESLA helium vessel with a nearly saturated bath of HeII
, where
Generalized steady-state limiting heat flux

## Slide 31: Sizing for HeII heat transfer
He vessel design: 2 K LHe heat transport
  Maximum heat flux: 1 W/cm2, no surface boiling
  Gap b/w cavity and he vessel, diameter of vertical tube
d
h
cavity
g
d
h
 | gap (cm)
HWR | 0.013
SSR1 | 0.038
SSR2 | 0.058
1 cm gap between cavity and helium jacket
He II heat transfer: sizing of helium jacket and chimney
 | HWR CMA | HWR CMB | SSR1 | SSR2
Total thermal load (W) | 14.0 | 26.1 | 29.6 | 112.7
Thermal load per cavity (W) | 7.0 | 6.5 | 9.9 | 18.8
Diameter of vertical tube (mm) | 37 |  | 44.7 | 60
Allowable thermal load (W) | 10.8 |  | 15.7 | 28.3

## Slide 32: Sizing for HeII heat transfer
Abnormal pressure fluctuation due to insufficient heat transfer area in superfluid helium
HWR CMB-#08
Qs per cavity ≒ 4.2 W
Qt of HWR-#52 ≒ 6 W
Qs per cavity ≒ 2.2 W
Qt of HWR-#74 ≒ 13.2 W while allowable thermal load is 10 W
 Fluctuation of pressure and liquid level

## Slide 33: Sizing for HeII heat transfer
Abnormal pressure fluctuation
HWR-#99 of HWR CMB-#18
Eacc = 6.6 MV/m, Qd= 9.6 W, Qt of #99 = 12.6 W
Pressure
Pressure
Eacc = 6.4 MV/m, Qd= 8.6 W, Qt of #99 = 11.6 W
Limiting heat flux is between 11.6 W and 12.6 W while the estimated one is 10.8 W

## Slide 34: Alignment of cavity
Requirement of cavity alignment
  x, y, z: ± 1mm (peak-to-peak), tilt: ± 0.28°
Cavities should be assembled precisely in the cryomodule
Position of cavity can be change by;
  Vacuum pumping: deformation of vacuum chamber
  Thermal contraction by cool-down: deformation of cavity, supporting system, etc.
   Position of cavity should be monitored or measured during vacuum pumping and cool-down

## Slide 35: Alignment of cavity
Fiducial post for laser tracker
Open target for cavity displacement measurement
Dressed cavity
Strong-back for cavity support
Connection to strong back
Beam port
Cavity position measurement during assembly
Lase tracker
Precision assembly in cyromodule

## Slide 36: Alignment of cavity
Displacement measurement by optical method
Measurement of cavity’s displacement before and after vacuum pumping and cool-down
Location of the beam port can be estimated by the displacement of the open targets
Micro Alignment Telescope (MAT)
Reference
Measurement of open target position before and after cool-down

## Slide 37: Alignment of cavity
Prototype test of displace measurement in the prototype cryomodule with LN2
Open targets on the beam ports to know the actual position of beam ports
To check the repeatability and to know the amount of vertical calibration

## Slide 38: Alignment of cavity
Repeatability of cavity position: QWR CM

## Slide 39: Alignment of cavity
Repeatability of cavity position: HWR CMB
Comparison of displacement of 1st and 3rd cool-down
Horizontal position of beam line can be estimated as the center line of left and right open target position
Vertical position of beam line can be estimated by the center line of left and right open target position and thermal contraction of cavity

## Slide 40: Alignment of cavity
Calibration of cavity’s vertical position for warm assembly
Fixed position for the cavity’s thermal contraction
Calibration value should include the displacement by the vacuum pumping and thermal contraction of supporting rod and cavity

## Slide 41: Alignment of cavity
Calibration of cavity’s vertical position for warm assembly
Calibration: 1.2 mm lower the beam port from the beam line (center line of gate valve)
In the 1st trial, error of beam port vertical position is less than 0.4 mm
In mass production, calibration value was changed considering the change of open target position based on the cool-down test results of cryomdoules.

## Slide 42
Results for mass production cryomodules
QWR CM
HWR CMA
HWR CMB
 | QCM | HCMA | HCMB
Vertical (mm) | -2.7 | -2.5 | -3.0
Horizontal (mm) | - | +1.0 | +1.0 (#1,#4) +1.8 (#2, #3)
Calibration value for each cryomdoule

## Slide 43
Contents
Introduction
Introduction on cryomodule
Design issue of cryomdoule
Mass production of SCL3 cryomodules
  Contract
  Schedule
  Changes in mass production
  Cavity fabrication
  Performance test
Installation and commissioning
1
2
3
4
5

## Slide 44: Mass production of SCL3 cryomdoule
Contracts
 | SCL31 |  | SCL32 | 
 | Products | Quantity | Products | Quantity
Final deliverables | QWR cryomodule | 22 | HWR cryomodule A | 15
 |  |  | HWR cryomodule B | 19
Subcomponents to be fabricated | Superconducting cavities | 18 | Superconducting cavities | 104
 | Power couplers | 20 | Power couplers | 104
 | Tuners | 22 | Tuners | 104
 | Cryostat | 21 | Cryostat A | 14
 |  |  | Cryostat B | 18
Contract amount | $ 9,065,128 |  | $ 25,457,148 | 
Period | 2017. 12 ~ 2020. 07 |  | 2018. 05 ~ 2022. 01 | 
Domestic vendor: VitzroTech
(cavity: RI as subcontractor)

## Slide 45: Mass production of SCL3 cryomdoule
Items supplied by IBS
 | QWR | HWR
Superconducting cavities | 4 ea | 2 ea
Power couplers | 2 ea | 2 ea
Tuner | - | 2 ea
Cryomodules | 1 set | 1 each sets
Nb materials | 120 % of required quantity | 
Cryogenic motors for tuner | 22 ea | 105 ea
Pick-up | 22 ea | 106 ea
Beam line gate valve | 40 ea | 68 ea
Cavity vacuum valve | 44 ea | 34 ea
Cryogenic valves | 42 ea | 96 ea
Temperature sensors | 210 ea | 820 ea

## Slide 46: Mass production of SCL3 cryomdoule
Acceptance test for final deliverable
 | QWR cryomodules | HWR cryomodules
Performance requirements | Total thermal load at 4.2 K below 20 W | Total thermal load at 2.05 K below 14.1 W (module A) below 26 W (module B)
Test conditions | Eacc: 6.1 MV/m Frequency: 82.15 MHz Cavity vacuum<5e-8 mbar Insulation vacuum<1e-5 mbar Resolution of frequency tuning< 5 Hz | Eacc: 6.6 MV/m Frequency: 162.5 MHz Cavity vacuum<5e-8 mbar Insulation vacuum<1e-5 mbar Resolution of frequency tuning< 5 Hz
Function test | Coupler: RF power supply more than 8 hours at room temperature Tuner: tuning range over 50 kHz Cavity alignment Operation of sensors, valves, and so on. | 
※ Vertical test must be done for all cavities before cryomodule assembly

## Slide 47
Schedule for mass production
 | 2017 | 2018 |  |  |  | 2019 |  |  |  | 2020 |  |  |  | 2021 |  |  | 
QWR |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
HWR |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Contract(‘17.12)
cavity fabrication (’18.03 ~ ‘20.06)
module & tuner fabrication (‘18.03~’19.03)
coupler fabrication (‘18.03 ~ ‘20.01)
vertical test (‘20.02 ~ ‘21. 07)
horizontal test (‘19.08 ~ ‘20. 09)
cavity fabrication (‘18.09~’21.06)
Contract(‘18.05)
module fabrication (‘18.12 ~ ‘20. 06)
tuner fabrication (‘19.01 ~ ‘20. 04)
coupler fabrication (‘19.03 ~ 21.04)
module assembly (‘19.07 ~ ‘20. 08)
module assembly (‘20.09 ~ ‘21.10)
horizontal test (‘20.10 ~ ‘21. 11)
vertical test (‘18.08 ~ ‘20.07)
Helium jacket issue based on the KGS (Korea Gas Safety)
Fabrication delay due to COVID-19 issue in subcontractor (RI, Germany)
Design change of beam sphere and beam port

## Slide 48: Changes in mass production
Reduction of df/dp of QWR cavity
 | Estimated (Hz/mbar) | Measured (Hz/mbar)
Prototype (bare) Beam port free | -37.9 | -33.4#2-1, -37#3-1 -31#3-2
Prototype (jacketed) Beam port free | 36.7 | 33.6#1-1, 36.5#2-1
Pre-production (jacketed) Beam port free | 12.7 | 13.97
Pre-production (jacketed) Beam port fixed | -4.6 | 5.2
 | A | B
Prototype | 115.7 | 148
Pre-production | 96.7 | 120
Force balance b/w cavity and helium jacket of cavity beam port
  Beam port-to-beam port length of the dressed cavity increases due to the helium pressure
  Reduction of outward force by reducing beam port flange size
F

## Slide 49: Changes in mass production
Uniform LFD of QWR cavity
 | Calculated [Hz/(MV/m)2] | Measured [Hz/(MV/m)2]
Prototype (bare) Beam port free | -16.4 | -20#1-1, -32.7#2-1 -17.4#2-2, -44.6#3-1 -14.7#3-2
LFD variation due to the welding of disk and rib on the top of the cavity
  Change the welding method from tack welding to line welding
QWR-#03(pre-production)
Before modification
(Cracks in welding point)
After modification
(Cracks in welding point)

## Slide 50: Changes in mass production
Beam port and beam sphere design change of HWR cavity
Parameter | Original | Modified
Rounding of Beam tube | 5mm | 10mm
H of Beamport cup | 52.5mm | 49.5mm
Diameter of Ring | 120mm | 130mm
Width of Ring | 65mm | 67mm
Rounding of Ring | 30mm | 33mm
Epeak/Eacc | 5.54 | 5.05
Chart: Eacc [MV/m]
| 6.6
Limit | 1450000000
HWR#1-RI-Jacket(Round type) @2K | 119000000 | 283000000 | 426000000 | 654000000 | 1030000000 | 1970000000 | 2980000000 | 3700000000 | 5190000000 | 6520000000 | 7190000000 | 7900000000 | 8340000000 | 8670000000 | 8970000000 | 8170000000 | 8450000000 | 8480000000 | 692000000 | 421000000 | 348000000 | 267000000 | 215000000 | 152000000 | 148000000
HWR#3-1-VZ-Jacket @2K | 6700000000 | 6670000000 | 6590000000 | 6570000000 | 6540000000 | 6530000000 | 6490000000 | 6450000000 | 6350000000 | 6200000000 | 6150000000 | 6030000000 | 5940000000 | 5860000000 | 5740000000 | 5560000000 | 5330000000 | 5040000000 | 4350000000 | 3990000000 | 3790000000 | 3460000000 | 2600000000 | 2110000000 | 1520000000 | 1230000000 | 986000000 | 795000000 | 637000000 | 457000000 | 368000000 | 290000000 | 236000000 | 195000000 | 163000000 | 139000000 | 122000000 | 123000000 | 37900 | 112000000 | 113000000
HWR#3-RT1 @2K | 11800000000 | 11800000000 | 11800000000 | 11900000000 | 11800000000 | 11800000000 | 11600000000 | 11500000000 | 11400000000 | 11300000000 | 11100000000 | 11300000000 | 11000000000 | 10600000000 | 10200000000 | 9570000000 | 8580000000 | 7390000000 | 6210000000 | 5160000000 | 4200000000 | 3410000000 | 2780000000 | 2280000000 | 1790000000 | 1430000000 | 1140000000 | 914000000 | 735000000 | 577000000 | 462000000 | 308000000
HWR#3-RT2 @2K | 13700000000 | 13600000000 | 13800000000 | 13600000000 | 13700000000 | 13500000000 | 13300000000 | 13300000000 | 12700000000 | 11600000000 | 9820000000 | 7920000000 | 6240000000 | 4870000000 | 3740000000 | 2880000000 | 2250000000 | 1750000000 | 1360000000 | 1050000000 | 833000000 | 654000000 | 410000000 | 512000000
Improvement EM performance of cavity
  FE starts around 6 MV/m while operating Eacc is 6.6 MV/m
  Decreasing Epeak/Eacc by 9.8 %
  Location of welding lines are moved away from the high Eacc region

## Slide 51: Changes in mass production
Round top for HWR cavity (during prototyping)
1st prototype
2nd prototype
2nd prototype
1st prototype
Flat top
Multipacting suppression: MP band below 2 MV/m
Structural stability of cavity w/o stiffener
  Deformation and stress reduced by half
  - Max. deformation: 1.9 mm  0.86 mm
  - Max. stress: 1.69 Gpa  679 MPa

## Slide 52: Cavity fabrication

## Slide 53: Cavity fabrication
Outer conductor
Inner conductor

## Slide 54: Cavity fabrication
Material
Material inspection
Visual inspection, Soaking test
Structural characteristics
Cutting of materials
Pressing & machining for parts

## Slide 55: Cavity fabrication
Bare cavity

## Slide 56: Cavity fabrication
Clamp-up test
Frequency adjustment before final welding
E-beam welding
Ultrasonic cleaning (USC)
BCP
HPR
High temperature heat treatment

## Slide 57: Cavity fabrication
1st BCP
2nd BCP
3rd BCP
Clean room assembly
Light BCP
(dressed cavity)
Visual inspection
Freq.,weight check
USC
(Liqinox, DI)
BCP
(Lower, ~50um)
USC
(DI water)
Drying
(10 class cleanroom)
Visual inspection
Freq.,weight check
BCP
(Upper, ~50um)
USC
(DI water)
Drying
(10 class cleanroom)
Visual inspection
Freq.,weight check
BCP
(Lower, ~50um)
HPR
Drying
(10 class cleanroom)
USC
(DI water)
Freq.,weight check
Cleaning
Ports & valve
assembly
Leak test
Ar charging
Vertical test
He jacketing
Visual inspection
Freq.,weight check
BCP
(Lower, ~20um)
HPR
Drying
(10 class cleanroom)
USC
(DI water)
Freq.,weight check
Full and light BCP procedure in detail
* Weight check: estimation of etching depth

## Slide 58: Cavity fabrication
Closed-loop chemical circulation type
49%HF+69%HNO3+85%H3PO4 (1:1:2)
Keeping Nb concentration in acid below 15g/L
Acid flow rate : 2~10LPM
Etch rate : 0.7~1㎛/min
Target removal : 120~150㎛(Bulk BCP) + 15~20㎛(light BCP, bare) + 15~20㎛(light BCP, jacketed)
Temperature control (23kW chiller) : below 15℃ during the process
  The acid is pre-cooled down to 5~9℃ in the acid storage tank. (cooling water temp. is just above freezing level of chiller)
BCP system

## Slide 59: Cavity fabrication
Visual inspection
USC
HPR
Drying
Clean assembly
Scratch, dent, oil
DI water, 50°C, 20 min.
Fixture installation
DI water quality check (18MΩ)
10 class cleanroom
HPR procedure in detail
Beam port
(5cm/min, 20rpm)
2ⅹHPR port
(5cm/min, 20rpm)
2ⅹHPR port
(5cm/min, 20rpm)
10 ~ 12 hours
HPR ports

## Slide 60
HPR system
Water pressure: 100 bar
Nozzle rotating speed : 20rpm
Nozzle/Cavity moving speed : 5cm/min
High pressure filter : 0.5㎛
Cavity fabrication

## Slide 61
USC (Ultrasonic cleaning) system
Class1000 (ISO6) cleanroom
Double bath type
  1st bath(degreasing) : 1% liquinox
  2nd bath(rinsing) : DI water
Ultrasonic Power : 1.5kW
Ultrasonic Frequency : 40kHz
Heating up to 60℃
Cavity fabrication

## Slide 62: Cavity fabrication
He jacketing procedure
Thermal shock test
(LN2)

## Slide 63: Cavity fabrication
Frequency Control during the whole fabrication
Chart: Frequency(MHz)
| clamp-up | weld cavity | initial tuning | BCP 1 | BCP 2 | BCP 3 | BCP 4 (final) | cold test (bared) @4.2K | weld jacket | light BCP | cold test (jacketed) @4.2K
Planned(5,6) | 80.952 | 81.008 | 81.008 | 81.038 | 81.068 | 81.098 | 81.125 | 81.25 | 81.125 | 81.14 | 81.265
QWR#1 | 81.045 | 81.112 | 81.1263 | 81.1397 | 81.2636
QWR#2 | 81.101 | 81.119 | 81.1606 | 81.2636
QWR#3 | 80.923 | 80.98 | 81.125 | 81.0683 | 81.1408
QWR#4 | 80.924 | 80.993 | 81.128 | 81.1327 | 81.1397
QWR#5 | 80.9465 | 81.054 | 80.9926 | 81.038 | 81.0695 | 81.1204 | 81.1204 | 81.241 | 81.1284 | 81.1482 | 81.2791
QWR#6 | 80.924 | 80.989 | 81.0538 | 81.0864 | 81.1228 | 81.1228 | 81.2384
QWR#7 | 80.952 | 81.0495 | 81.006 | 81.031 | 81.0619 | 81.0955 | 81.1382 | 81.265
QWR#8 | 80.962 | 81.0519 | 81.0093
QWR#9
QWR#10 | 80.906 | 80.9883 | 81.0134 | 81.0521 | 81.0979 | 81.128 | 81.13 | 81.1423
QWR#11 | 80.93 | 81.0076 | 81.0319 | 81.0643 | 81.0911 | 81.1239 | 81.249 | 81.126 | 81.14
Target: 81.14 MHz ±10kHz before assembly in cryomodule

## Slide 64
Clean assembly
Cavity fabrication
USC & HPR
Parts using USC | Parts not using USC
Less than 1 particle (≤ 0.3μm) /5s | Less than 1 particle (≥ 1.0 μm) /1s
Particle counting
Reference: TTC topical workshop on clean room assembly, 2014

## Slide 65: Performance Test
Vertical Test
Vertical Test
Cryostat
4K Reservoir
Vacuum Line
2K Reservoir
Vacuum Chamber
Ion Pump
Top flange

## Slide 66: Performance Test
Vertical Test
Vertical Test
Ion pump
Cryogenic valve
Vacuum pumping lines
& vacuum gauges
Feedthroughs
Assembly area(clean room) for vertical test
Top flange in the vertical test pit
Vacuum pump
for cavity
GHe supply & return
VLP return
LN2 supply & return

## Slide 67
Variable coupler
Motor
Inner conductor
Outer conductor and bellows
Vertical Test

## Slide 68
QWR VT results
Eacc: 6.1 MV/m, Q0=2.4e+8@4.2K, Number of cavity: 22 ea

## Slide 69
QWR VT results
Acceptance rate: 56 % (18 pass / 32 test, 4 prototype cavity)
  Failure for multipacting conditioning due to insufficient baking of variable coupler
  Field emission due to contamination
Baking of cavity and variable coupler

## Slide 70
HWR VT results
Eacc: 6.6 MV/m, Q0=2.3e+9@2.05K, Number of cavity: 106 ea

## Slide 71
HWR VT results
Acceptance rate: 76 %
  FE: 28 cases, MP failure: 3 cases, Vacuum failure: 3 cases, Malfunction of V/C: 2 cases

## Slide 72
Performance vs. processing
① Hand HPR and baking for variable coupler (’19.12)  overcoming MP failure
② N2 purging before the vacuum line connection (‘20.04)
③ 100 bar HPR for variable coupler bellows to prevent contamination of cavity(‘20.05)
④ Cleanroom management: cleaning tools, clothes, etc. (‘20.06)

## Slide 73: Horizontal Test
Horizontal Test
Test Procedure
Installation in the bunker
Cavity frequency check & tuner operation test
Leak test and vacuum pumping for cavity
Leak test and Purging cryogenic pipes
Connecting cryogenic lines, signal cables, DC bias,
RF transmission lines, etc
Cool-down
Thermal shield cool-down by LN2
Cavity cool-down through cool-down line
4K Test
MP conditioning
Cable calibration
Static and total thermal load measurement
Field emission conditioning with pulsed RF power,
if necessary
2K Test
2 K pump-down: df/dp measurement (~3MV/m)
Qext measurement with VNA
Static and total thermal load measurement
LFD & tuner operation test
Alignment measurement
Tuner test at room temp. (~0.2 Hz/pulse, ~30 kHz span)

## Slide 74
Horizontal test facility
Valve box for HT
SSPA
RF transmission line
Helium distribution lines
Horizontal test bunkers

## Slide 75: Performance Test
Horizontal Test
Test setup

## Slide 76: Performance Test
Horizontal Test
P&ID for cryomodule and cryogenic system
Thermal shield cooled by LN2
Thermal intercepts
- 4 K intercepts: loop thermosiphon connected with 4 K reservoir
- 40 K intercepts: copper braid wire connected with thermal shield
3 cryogenic valves: 1 for cool-down and 2 for JT expansion
Heat exchanger to precool the LHe before 2 K expansion
Vacuum pumping system to maintain 35 mbar
Liquefier (280L/h) and dewar(3,000L)
Recovery compressor and gas bag
Pump-down system(vacuum pumps): 1.5g/s each

## Slide 77
Cool-down of cryomodule
Initial LHe cooling through a cool-down line
Cool-down history of HWR cryomodule

## Slide 78
Multipacting conditioning (HWR cavity)
Pt
Vaccum
Pf
Eacc
MP in low field (<1MV/m)
- Pf below 40 W
- Vacuum level fluctuation
Pf
Pr
Pt
Eacc

## Slide 79
Multipacting conditioning (HWR cavity)
Pt
Eacc
Vaccum
Pf
Pf
Pr
Pt
Pf increases in stepwise but Pr decreases
MP in high field (<2MV/m)

## Slide 80
Conditioning effect during Eacc increase
Conditioning of cavity (Burning of field emitter)
Eacc (Mv/m) | 3.5 | 4.0 | 4.5 | 5.0 | 5.5 | 6.0 | 6.6 | Remarks
HWR#13 (uSv/hr) | 8.5 | 48 | 352 | 800 | 3450 |  |  | Trip on 5.6
 | After trip → |  | 0.7 | 8 | 56 | 300 | 1250 | 
HWR#32 (uSv/hr) | 4 | 89 | 223 | 400 |  |  |  | Trip on 5
 | After trip → |  |  | 65 | 300 | 430 | 1800 | 
X-ray: amount of field emission
 quick view of cavity’s performance

## Slide 81
2K pump-down
2K pump-down
Phase transition around λ-point
4.2 K @ 1bar
2.05 K @ 35mbar
Pressure
Cavity temperature
df/dp measurement during 2K pump-down (Eacc < 3MV/m)
LHe level

## Slide 82
Qext measurement with VNA
H. Hahn et al., Calibration of the ERL cavity FPC and PU couplers, 2010
CM number | HWR #B07 |  |  | 
CAV | HWR #51 | HWR #77 | HWR #80 | HWR #81
Freq [MHz] | 162.5 | 162.5 | 162.5 | 162.5
S21 (dB) | -52.22 | -52.05 | -51.19 | -50.91
S21 | 2.45E-03 | 2.50E-03 | 2.76E-03 | 2.85E-03
QL | 1.07E+06 | 8.01E+05 | 9.98E+05 | 1.13E+06
S11 (dB) | -6.00E-02 | -8.00E-02 | -7.00E-02 | -6.00E-02
S11 | 9.93E-01 | 9.91E-01 | 9.92E-01 | 9.93E-01
S22 (dB) | -4.70E-01 | -3.80E-01 | -3.90E-01 | -4.40E-01
S22 | 9.47E-01 | 9.57E-01 | 9.56E-01 | 9.51E-01
Qt | 7.13E+11 | 5.14E+11 | 5.25E+11 | 5.58E+11
S21’ (dB) | -51.96 | -51.82 | -50.96 | -50.66
S21’ | 2.52E-03 | 2.56E-03 | 2.83E-03 | 2.93E-03
Qt’ | 6.71E+11 | 4.87E+11 | 4.98E+11 | 5.27E+11
, since

## Slide 83
Qext measurement of QWR and HWR cavities
Requirement for Pickup Qext(Qt) from LLRF system: two orders higher than Q0
Power coupler Qext (Qc): control bandwidth and required RF power
- Average control bandwidth: QWR (149 Hz), HWR (143 Hz)
QWR
HWR

## Slide 84
Thermal load measurement
Measurement of thermal loads
LFD measurement
Eacc2 [(MV/m)2]
Frequency [Hz]
Thermal load measured by boil-off calorimetry
Dynamic thermal load of each cavity
, where is thermal load when only one cavity is in its operating Eacc

## Slide 85
df/dp and LFD measurement
df/dp and LFD measurement results
Comparison of VT and HT
Relatively larger df/dp of HWR cavities but lower pressure fluctuation at 2.05 K
- Pressure fluctuation: ~ ±1 mbar at 4.5 K, ~ ±0.3mbar at 2.05 K
Enhancement of cavity’s stiffness by tuner in cryomodule: 45 % lower df/dp and LFD
Prototype cavity

## Slide 86
Thermal load measurement results
Dynamic thermal load of each cryomodule is sum of the dynamic thermal load of cavities in the cryomdoules

## Slide 87
Static thermal load
Main reason: Large mass (~40 Kg) of tuner
Static thermal load that we had measured were 5.6 W and 8.3 W for HWR CMA and HWR CMB, respectively while the average static thermal load measured during the experiments were 8.0 W and 10.7 W, respectively.
Static thermal load change w.r.t. time during HT
Average static thermal load
- HT: QWR (10.4 W), HCMA (9.6 W), HCMB (9.5 W)
 NOT THERMALIZED!!!
- Tunnel: QWR (4.5 W), HCMA (4.3 W), HCMB (6.1 W)
Static thermal load of HT vs. tunnel
Wrong measurement

## Slide 88
Dynamic thermal load of each cavity

## Slide 89
Thermal load measurement of QWR cryomdoule in tunnel
Eacc of QCM #01~#06 (ramp-up section): 4 MV/m (Qt < 1 W @ 4 MV/m)
Malfunction of level meter of QCM#14, QCM#21
Severe degradation of cavities in QCM #13, #14

## Slide 90
Tuner test
Wide range test (±100 Hz span)
- 20 pulse/step * 50 steps * 3 times up and down
- Control bandwidth ~ 130 Hz
- Tuning resolution: 0.2~0.25 Hz/pulse

## Slide 91
Narrow range test
- 20 pulse/step * 3 steps * 20 times up and down
- Small backlash (~a few Hz)
Tuner test

## Slide 92
Tuner test
FRQ-DOWN
FRQ-UP
df Measurement
FRQ-UP
FRQ-DOWN
df Measurement
Noise during the operation of tuner (df of cavity ~ 300 Hz)
- Noise removed by reducing the motor speed to 1/32

## Slide 93
Phase and amplitude locking test of cryomdoule

## Slide 95
Contents
Introduction
Introduction on cryomodule
Design issue of cryomdoule
Mass production of SCL3 cryomodules
Installation and commissioning
  Installation
  Beam commissioning
1
2
3
4
5

## Slide 96: Installation

## Slide 97: Installation
Cryomodule and warm section is clean assembled in the portable clean booth in tunnel
Particle counts (size=0.5um above/10min.) were less than 30 counts

## Slide 98: Installation
Welding VBx to CM
VBx connection
QWR CMs, VBx in rear side
Cryogenic systems
Warm compressors
LHe distribution box
Cold box
SCL3 plant: 4.2 KW at 4.5 K, SCL2 plant: 13.5 kW at 4.5 K

## Slide 99: Beam commissioning
Injector
SCL31: 22 QWR cryomodules
(‘22.12.16) SCL31 beam commissioning
(‘22.10.07) 5 QWR cryomodules
SCL31 section: Ar beam (2.47 MeV/u, 34 uA)
Beam commissioning of whole SCL3 is on-going
  MP conditioning of 76 HWR cavities were finished.
  Beam commissioning for SCL3: ‘23. 3. 24
  SCL3-KoBRa beam commissioning: ‘23. 4. 14
  Warm-up and maintenance: ~ ‘23. 8. 31
  - QWR#20, HWR CMA-#1, HWR CMB-#11
  - VLP return cryogenic valves in VBxs
  Experiment in KoBRA: ’23. 12. 01 ~
14.5GHz ECR-IS
RFQ
LEBT
MEBT

## Slide 100
Thank you

## Slide 101: Sizing for HeII heat transfer
Increase of JT valve opening
Abnormal pressure fluctuation: other reason??
Sudden stop of pumping

## Slide 102
Pulse conditioning
X-ray
Pf
Pr
Pt
Quench
High Eacc without quench
(Max. Pout of SSPA = 4 kW)
Monitoring X-ray value
Pt signal in oscilloscope